This is a simple 3 band WARC dipole made by Vinko S53F.

Used wire - 2mm diameter!!!! copper wire (exactly this diameter for the given length! or cca 3,14mm2)

All the 3 wires are connected togeather (there is no parasitic dipoles). The vertical parts of the outer dipoles are the same length as the spacing and they are added to the horizontal length of the dipoles (applied to the dipoles for 30 and 12m)

So the total lengths of one side of the dipoles are:

30m - 6,86m

17m - 3,86m

12m - 2,85m

We used plastic spacers with holes to have the right distance between the dipoles.