A homemade receiver for GPS & GLONASS satellites
        ************************************************


             Matjaz Vidmar, S53MV (ex YU3UMV, YT3MV)






1. Introduction to GPS & GLONASS
================================
     Radio amateurs have always been interested in space
technology, since the latter strongly depends on reliable
radio communications. Of course radio amateurs are not
only interested in amateur-radio satellites: almost any
artificial Earth's satellite represents a challenge, either to
receive its weak signal on rather high frequencies or to
demodulate, decode and use the data it is transmitting.
     Besides amateur-radio satellites, the most interesting
satellites for radio amateurs are weather (imaging) satellites:
radio amateurs have succesfully built weather-satellite image
reception equipment for all known weather satellites and all
known image transmission standards. Radio-amateurs also
pioneered satellite TV reception using small antennas much
earlier than this became a mass-produced consumer product.
     Although the first navigation satellites were launched
more than 30 years ago, satellite navigation and positioning
has only become popular in the last few years with the
introduction of reliable, accurate and easy-to-use systems
like the american Global Positioning System (GPS) and the
russian GLObal NAvigation Satellite System (GLONASS).
Both are intended to replace a variety of ground-based
radio-navigation aids and as a side product, to provide any
suitably equipped user with very accurate time (100ns) and
very accurate frequency (10^-12).
     Although both GPS and GLONASS are primarily intended
for military users, there are already more civilian users of
these systems. GPS (and soon combined GPS/GLONASS) navigation
receivers can be made small, light-weight, easy-to-operate
and inexpensive like VHF FM "handie-talkie" transceivers.
Since these receivers can measure their tri-dimensional
position with an accuracy of around 50m anywhere on the
Earth's surface, their user community ranges from
pleasure-aircraft pilots to truck drivers and mountain
climbers and, why not, radio amateurs!
     Besides the challenge to build a satellite receiver
radio amateurs can use GPS and GLONASS signals in other ways
as well. The most immediate application of a GPS or GLONASS
receiver is certainly as a highly accurate frequency source.
Accurate timing and synchronization may be required for
advanced communication techniques like coherent communications
or to seriously investigate the propagation path and the
propagation mechanism of radio waves. Finally, positioning
and direction-finding may be useful for high-gain microwave
antenna pointing.
     In this article I am first going to describe the



l- 2 -
l
satellites and the radio signals they are broadcasting.
Further I am going to describe the principles of operation of
a GPS or GLONASS receiver. Finally I am going to describe the
practical construction of homemade GPS and GLONASS receivers,
together with their operating software. These receivers can
be built in two different forms: as stand alone, portable
receivers with a small keyboard and a LCD display, or as
peripherals with their own plug-in modules for the "DSP
computer" described in [1] and [2].





















































l- 3 -
l
2. GPS & GLONASS system description
===================================

2.1. Radio-navigation principles
--------------------------------
     Radio navigation evolved together with other applications
of radio waves. The operation of all radio-navigation systems
is based on the assumption that the propagation mechanism of
radio waves is well known and that the propagation speed of
radio waves is usually very close to the speed of light in free
space. Further, systems using radio waves usually have a
sufficient range to be practically useable for position,
velocity and attitude determination of a remotely-located
user. Finally, all of the measurements on radio waves, like
direction finding, time-delay measurements, phase measurements
or Doppler-shift measurements, can be performed with simple
and inexpensive technical means at least on the user side.
     Early radio-navigation systems used the directional
properties of the receiving antenna, transmitting antenna or
both. In these systems the main sources of measurement errors
are the inaccuracies of the antenna pattern(s). Since the
measured quantity is an angle, the position error grows
linearly with increasing the distance between the remote user
at an unknown location and the navigation equipment at known
location(s). Such systems are therefore severely limited in
either the range or the accuracy and are only efficient to
bring a user to a single point, like bringing an aircraft to
the beginning of a landing runway using the Instrumented
Landing System (ILS).
     Time or frequency are certainly the physical quantities
that can be measured most accurately. If the propagation speed
and propagation mode of radio waves are known, one can easily
compute the distance from a time-delay measurement. Further,
the absolute accuracy of such distance measurements does not
depend on the order of magnitude of the distances involved,
except for the uncertainties in the propagation speed of
the radio waves used. Therefore, all long-distance, precision
radio-navigation systems are based on time-delay (or signal
phase difference) measurements and/or the time derivatives
of these quantities, usually observed as the Doppler frequency
shift.
     The easiest way to measure the distance to a known site
is to install a radio repeater there, transmit a signal,
receive the answer from the repeater and measure the round-trip
time. Although such radio-navigation systems were practically
implemented (like DME for civilian aircrafts), they have some
limitations due to the fact that the user needs both to
transmit and to receive radio signals. Such a system can not
accomodate an unlimited number of users since only one user
can use the radio repeater at a time and each measurement
takes some time. Some military users may also not want to
transmit any radio signals to avoid disclosing their position
to the enemy while civilian users do not want the requirement
of having their navigation equipment licensed.
     The transmit requirement for the user can be dropped if
the user can acheive and maintain synchronization with the
navigation transmitters in a different way. For example,
both the user and the navigation transmitters may be equipped
with high-accuracy time/frequency sources like atomic clocks.



l- 4 -
l
The user then synchronizes his clock at a known location and
the same clock is then used at an unknown location for
time-delay measurements.
     Since atomic clocks are expensive, bulky and power-hungry
devices, a more simple alternative is desired for navigation
systems serving a large number of passive, receive-only users.
Such a system must have a number of synchronized transmitters
as shown on Fig. 1. Since the user does not know the accurate
time, he can not measure the time delays and the distances
d1, d2, d3... to the transmitters TX1, TX2, TX3... directly.
     The user can only measure the differences in the
times-of-arrival of different TX signals. Time differences
correspond to distance differences. The set of points
corresponding to a given distance difference from two
given points is a hyperbola (in two dimensions) or a
rotational hyperboloid (in three dimensions). The two
transmitters are located in the focal points of the
hyperbola (rotational hyperboloid).
     For two-dimensional navigation (positioning) signals from
at least three synchronized transmitters need to be received.
For example, from the measured time difference between TX1 and
TX2 the user can plot the hyperbola d1-d2=const.12 on his map.
Similarly, from the measured time difference between TX2 and
TX3 the user can plot the hyperbola d2-d3=const.23 on his map.
The two hyperbolas intersect in a point corresponding to the
unknown user location!
     For three-dimensional navigation signals from at least
four synchronized transmitters need to be received. The three
independent time differences generate three different
rotational hyperboloids. Rotational hyperboloids are curved
surfaces. Two of them intersect in a curved line which in turn
intersects with the third hyperboloid in a point corresponding
to the unknown three-dimensional user position.
     If there are more transmitters available, the user can
select the best set of three (four) that provide two
hyperbolas (three rotational hyperboloids) intersecting as
close as possible under a right angle(s). The remaining
transmitters can then be used to check for errors and/or
ambiguous solutions, since with curved lines and surfaces
there can be more than one intersection point.
     Hyperbolic navigation systems were first implemented
as ground-based navigation systems operating in the
medium and longwave radio frequency spectrum like LORAN,
DECCA or OMEGA. Since the transmitters are located on the
Earth's surface, the geometry of the problem does not allow
a three-dimensional navigation. These systems only measure
the longitude and latitude reliably. To measure the altitude,
one of the transmitters should be located above or below the
user's receiver or at least out of the user's horizon plane.
     Ground-based radio-navigation systems use relatively
low frequencies of the radio spectrum to acheive a large
radio range and avoid undefined skywave (ionospheric)
propagation at the same time. For example, OMEGA uses the
frequency range between 10 and 14kHz to acheive world-wide
coverage with just 8 (eight) transmitters!
     Longwave radio-navigation systems were designed when
digital computers were not readily available yet:
two-dimensional navigation with fixed transmitter sites only
requires a minimum of computations to be performed by the user.



l- 5 -
l
The families of hyperbolas for each transmitter pair can be
directly plotted on maps, including corrections for known
propagation anomalies.
     One of the first applications of artificial satellites
was radio navigation. Obviously artificial satellites need
radio navigation themselves, to evaluate the performance of
the rocket carrier and determine the final satellite's orbit.
On the other hand, the space environment is an ideal place
for navigation transmitters, since a large radio range can be
acheived at VHF and higher frequencies where the propagation
of radio waves is predictable and the influence of the
always-changing ionosphere is marginal. Finally, the location
of navigation transmitters in space can be chosen so that
three-dimensional navigation is possible everywhere on the
Earth's surface.
     Since initially the satellites could only be launched in
low-earth orbits, the first navigation satellites were launched
in low, 1000km altitude, polar orbits, like the american
TRANSIT satellites or the soviet equivalent TSIKADA. Since a
satellite in a low-Earth orbit is quickly moving along its
orbital track, a single satellite may be used for position
determination. While even a simple crystal-controlled user's
clock is sufficiently accurate for a few minutes, the satellite
significantly changes its position on the sky and this is
roughly equivalent to several navigation transmitters at
several different sites along the orbital track.
     In practice the user simply measures the Doppler shift on
the satellite's signal for a certain period of time and
computes his unknown position from the result of this
measurement and the satellite's orbital data. Although a
single satellite is required for position determination,
these systems usually have from six (TRANSIT) up to twelve
satellites to improve the coverage, since a low-Earth orbit
satellite is only visible for a limited amount of time for a
user located on the Earth's surface. Since the ionosphere
still has some effect on VHF and UHF radio waves, both
american and soviet satellites transmit on two frequencies
around 150MHz and around 400MHz. The actual channel frequencies
are kept in the precise ratio 3/8 and the transmitters are
kept coherent to allow for ionospheric corrections.
     The drawbacks of low-Earth orbit navigation satellites
are that the user may have to wait for a satellite pass and
even then the measurement takes several minutes. Finally,
the user velocity, both magnitude and direction, must be known
and compensated-for in the position computation. To allow an
almost istantaneous position determination more satellites are
required. If a user has at least four visible satellites in
different parts of the sky, he can compute his
three-dimensional position istantaneously, without having to
wait for the satellites to move across the sky.
     In order to limit the number of satellites required,
these have to be launched to higher orbits. Such satellite
navigation systems are the american GPS and the soviet GLONASS
that should acheive world-wide coverage with 24 satellites
each when completed. Both systems should provide at least
four visible satellites in any part of the world including
in-orbit spares and a suitable distribution of the visible
satellites on the sky to allow a three-dimensional
navigation.



l- 6 -
l
     Finally, one should notice that satellite navigation
systems require a large amount of computations to be performed
by the user. The satellites continuously change their
positions, so no hyperbolas could be plotted on maps.
Three-dimensional navigation is even more demanding, so that
a digital computer is absolutely necessary. Maybe this
explains why satellite positioning only became popular a few
years ago: although navigation satellites were available for
more than 30 years, inexpensive computers were not!

2.2. Satellite navigation equations
-----------------------------------
     In order to understand satellite navigation systems one
should first look in the mathematical background of satellite
navigation. To perform any practical computations one should
define a coordinate system first. Most satellite navigation
systems use a right-hand cartesian coordinate system like the
one shown on Fig. 2. The coordinate system is body-fixed to
the Earth and is therefore a rotating coordinate system,
unlike the inertial coordinate system used for keplerian
orbital elements for most satellites.
     Usually, the origin of the coordinate system is the
Earth's center of mass. The Z-axis of the coordinate system
corresponds to the Earth's rotation axis and the Z-axis is
pointing north. The X-axis and Y-axis are in the equatorial
plane and the X-axis points in the direction of the Greenwich
meridian while the Y-axis is oriented so that a right-hand
orthogonal coordinate system is obtained.
     However, if the user prefers a more conventional
coordinate system, like longitude, latitude and altitude
above sea level (altitude above the surface of an ellipsoid),
he can always perform the required transformations. These
transformations are always performed on the final result,
since most of the internal computations of a navigation
receiver are most easily performed in a cartesian coordinate
system.
     Finally, one should understand that there are several
different coordinate systems in use although the basic
definition is the same for all of them. Satellite navigation
systems improved the absolute positioning accuracy down to
the 1m (one meter) level, so the differences between several
local geographic coordinate systems have become noticeable.
For example, GPS is using the WGS-84 coordinate system
while GLONASS is using the SGS-85 coordinate system. The
difference between these two systems is around 10m in the
east-west direction and around 10m in the up-down direction
at the author's location in central Europe.
     Using vector notation one can write down the naviagtion
equations in an orderly way. In a three-dimensional cartesian
coordinate system it is easy to understand that a single
vector includes three independent quantitites.
     A time-difference navigation equation only includes the
range vectors representing the positions of the transmitters
(satellites) and of the receiver (user). Distances between
the user and the satellites are computed as magnitudes
(absolute values) of range vector differences. On the other
side of the equation we find the measured time difference
multiplied by the propagation velocity of radio waves (c).
     If the user location - user range vector - is unknown,



l- 7 -
l
this represents three scalar unknowns that require three
independent time-difference (scalar!) equations for the
solution. To obtain three independent equations at least four
transmitters are required. The solution of these equations is
not straightforward since the absolute value of a vector is a
non-linear function: it contains squaring and square-root
operations. The navigation equations are therefore usually
solved in a numerical iterative procedure, although an
analytical solution exsists [3].
     A Dopplershift-difference navigation equation includes
both range vectors and velocity vectors since to compute the
Doppler frequency shift one has to obtain the velocity
difference first and then compute the projection of the
velocity difference vector on the direction of propagation of
radio waves. Vector projections are computed using the
scalar (dot) product between two vectors. On the other side of
the equation we find the measured Doppler-shift difference
in relative units, the absolute difference being divided by
the nominal carrier frequency (f0). The relative frequency
difference is then converted to velocity units by multiplying
it by the propagation velocity of radio waves (c).
     The Doppler-difference navigation equations include
the user position vector and the user velocity vector and
these can be both unknown representing up to six scalar
unknowns. Since one usually does not have available six
independent Doppler-difference equations, these are usually
used in the following ways:
(1) If the user position is already available from
    time-difference equations, the user velocity vector
    can be computed from three independent Doppler-difference
    equations.
(2) If the user velocity vector is known or the user velocity
    is zero (stationary user), then the user position can be
    computed from three independent Doppler-difference
    equations.
(3) Various combinations of time-difference and
    Doppler-difference equations are also possible.
     Besides the visibility problem, the navigation equations
put some additional constraints and desirable features for
navigation satellite orbits. The final accuracy of the
navigation solution, position or velocity, depends on the
conditioning of the system of equations. An ill-conditioned
system of equations will amplify any measurement errors in
the final result. A geometrical equivalent of an
ill-conditioned system of equations is when lines or surfaces
(rotational hyperboloids) intersect at very low angles.
     The accuracy degradation due to poor conditioning of the
system of equations is usually called Geometrical Dilution Of
Precision (GDOP). Of course the satellite orbits have to be
chosen to provide the lowest possible GDOP to the widest user
community: since the equations are non-linear, GDOP changes
with the user position. The users themselves have to chose the
best set of four satellites to get the lowest GDOP, since more
satellites may be visible, even at high elevations, but
providing a large GDOP.
     The most obvious cause of a large GDOP with a system of
time-difference equations is when two satellites are close
together on the sky. A more general case is when all four
satellites are almost in a single plane. For the same reason



l- 8 -
l
the geostationary orbit is not very suitable for navigation
satellites. The geostationary orbit has yet another
disadvantage for navigation satellites: the relative velocity
of the satellite is very low for Earth-located users and the
Doppler-difference equations themselves (not the system!) are
ill-conditioned, since the unknown user position vector is
multiplied by very small numbers.

2.3. GPS & GLONASS satellite systems
------------------------------------
     GPS and GLONASS are the first satellite systems that
require the simultaneous operation of a number of satellites.
In other satellite systems, including earlier navigation
systems, the operation of every single satellite was almost
autonomous and any additional satellites only improved the
capacity of the system. In GPS or GLONASS the satellites
need to be synchronized and can only perform as a
constellation of at least four visible satellites for every
possible user location without forgetting the GDOP
requirement!
     Both GPS and GLONASS satellites are launched into similar
orbits. A comparison among GPS, GLONASS and more popular
satellite orbits like the geostationary orbit or the retrograde
sun-synchronous Low-Earth Orbit (LEO) is made on the scale
drawing on Fig. 3. Both GPS and GLONASS satellites are launched
into circular orbits with the inclination ranging between 55
and 65 degrees and the orbital period in the order of 12 hours,
which corresponds to an altitude of around 20000km (one and a
half Earth diameters).
     The GPS system was initially planned to use three
different orbital planes with an inclination of 63 degrees and
the ascending nodes equally spaced at 120 degrees around
the equator. Each orbital plane would accomodate 8 equally
spaced satellites with an orbital period of 11 hours and
58 minutes, synchronized with the Earth's rotation rate [4].
During a 10-year test period from 1978 to 1988 only 10 such
"Block I" satellites were successfully launched in orbital
planes "A" and "C" as shown on Fig. 4.
     The GPS specification was changed afterwards [5] and the
new "Block II" satellites are being launched in 55-degrees
inclination orbits in six different orbital planes A, B, C, D
E and F, with the ascending nodes equally spaced at 60 degrees
around the equator. The new GPS constellation should also
include 24 satellites, having four satellites in each orbital
plane, incluiding active in-orbit spares. The orbital period
of the GPS satellites should be increased to 12 hours to avoid
repeat-track orbits and resonances with the Earth's gravity
field.
     Finally, the new "Block II" satellites also include a
nasty feature called "Selective Availability" (SA): the
onboard hardware may, on ground command, intentionally degrade
the accuracy of the navigation signals for civilian users
while military users still have access to the full system
accuracy. Beginning in 1988 and up to March 1993, 9 GPS
"Block II" and 10 new GPS "Block IIA" satellites have been
launched using "Delta" rockets. The SA-mode is currently
turned on and degrades the accuracy to betweem 50 and 100m.
     The GLONASS system is planned to use three different
orbital planes with an inclination of 64.8 degrees and the



l- 9 -
l
ascending nodes equally spaced at 120 degrees around the
equator. Each orbital plane would accomodate 8 (or 12)
equally spaced satellites with an orbital period of 11 hours,
15 minutes and 44 seconds, so that each satellite repeats its
ground track after exactly 17 revolutions or 8 days [6].
     Since the beginning of the GLONASS program a large number
of satellites have been launched into GLONASS orbital planes
1 and 3, the orbital plane 2 has not been used yet. Some
satellites never transmitted any radio signals, since the
GLONASS system also includes passive "Etalon" satellites used
as optical reflectors for accurate orbit determination.
GLONASS satellites are launched three at a time with a single
"Proton" rocket. Due to this constraint all three satellites
can only be launched in the same orbital plane.
     Recently observed GLONASS satellite operation is shown
on Fig. 5. The observed lifetime of GLONASS satellites
seems to be shorter than that of american GPS counterparts.
A critical piece of onboard equipment are the atomic clocks
required for system synchronization. Although each satellite
carries redundant rubidium and cesium clocks, these caused
the failure of many GPS and GLONASS satellites. In addition to
this, GLONASS satellites have had problems with the on-board
computer. Unfortunately, the GPS or GLONASS orbit altitude is
actually in the worst ionizing-radiation zone, the same
radiation that already destroyed the AMSAT-OSCAR-10 computer
memory.

2.4. GPS & GLONASS satellite on-board equipment
-----------------------------------------------
     Since the two systems are similar, GPS and GLONASS
satellites carry almost the same on-board equipment as shown
on Fig. 6. For the navigation function alone, the satellites
could be much simplier, carrying a simple linear transponder
like on civilian communications satellites. The required
navigation signals could be generated and synchronized by a
network of groundstations.
     However, both GPS and GLONASS are primarily intended as
military systems. Uplinks are undesired since they can be
easily jammed and a network of groundstations can be easily
destroyed. Therefore, both GPS and GLONASS satellites are
designed for completely autonomous operation and generation
of the required signals. Synchronization is maintained by
on-board atomic clocks that are only periodically updated
by the groundstations.
     Both GPS and GLONASS satellites carry a cesium atomic
clock as their primary time/frequency standard, with the
accuracy ranging between 10^-12 and 10^-13. Much smaller
and lightweight rubidium atomic clocks are used as a backup
in the case the main time/frequency standard fails, although
rubidium atomic clocks are an order of magnitude less
accurate. Due to the stable space environment these atomic
clocks usually perform better than their ground-based
counterparts and any long-term drifts or offsets can be easily
compensated by uploading the required correction coefficients
in the on-board computer.
     The output of the atomic time/frequency standard drives a
frequency synthesizer so that all the carrier frequencies and
modulation rates are derived coherently from the same
reference frequency.



l- 10 -
l
     The on-board computer generates the so-called navigation
data. These include information about the exact location
of the satellite, also called precision ephemeris, information
about the offset and drift of the on-board atomic clock and
information about other satellites in the system, also called
almanac. The first two are used directly by the user's
computer to assemble the navigation equations. The almanac
data can be used to predict visible satellites and avoid
attempting to use dead, malfunctioning or inexsistent
satellites, thus speeding-up the acquisition of four valid
satellite signals with a reasonable GDOP.
     Besides the transmitters for broadcasting navigation
signals, GPS and GLONASS satellites also have telecommand and
telemetry radio links. In particular, the telecommand link is
used by the command stations to regularly upload fresh
navigation data into the on-board computer. Usually this is
done once per day, although the on-board computer memory can
store enough data for several weeks in advance. In addition to
dedicated telemetry links, part of the telemetry data is also
inserted in the navigation data stream.

2.5. GPS & GLONASS satellite transmissions
------------------------------------------
     GPS and GLONASS satellites use the microwave L-band to
broadcast three separate radio-navigation signals on two
separate RF channels usually called L1 (around 1.6GHz) and
L2 (around 1.2GHz). These frequencies were chosen as a
compromise between the required satellite transmitter power
and ionospheric errors. The influence of the ionosphere
decreases with the square of the carrier frequency and is
very small above 1GHz. However, in a precision navigation
system it still induces a position error of about 50m at
the L1 frequency during daylight and medium solar activity.
     On the other hand, GPS and GLONASS were designed to work
with omnidirectional, hemispherical-coverage receiving
antennas. The capture area of an antenna with a defined
radiation pattern decreases with the square of the operating
frequency, so the power of the on-board transmitter has to be
increased by the same amount.
     Both GPS and GLONASS broadcast two different signals:
a Coarse/Acquisition (C/A) signal and Precision (P) signal.
The C/A-signal is only transmitted on the higher frequency
(L1) while the P-signal is transmitted on two widely-separated
RF channels (L1 and L2). Since the frequency dependence of
ionospheric errors is known, the absolute error on each
carrier frequency can be computed from the measured difference
between the two P-transmissions on L1 and L2 carriers.
     The L1 C/A- and P-carriers are in quadrature to enable a
single power amplifier to be used for both signals, as shown
on Fig. 6. The L1 and L2 transmitter outputs are combined in
a passive network and feed an array of helix antennas. These
produce a shaped beam covering the whole visible hemisphere
from the GPS/GLONASS orbit with the same signal strength.
     All three GPS or GLONASS transmissions are continuous,
straightforward BPSK modulated carriers. Pulse modulation is
not used. The timing information is transmitted in the
modulation: the user's receiver measures the time of arrival
of a defined bit pattern, which is a known code. If desired,
the modulation code phase can be related to the carrier phase



l- 11 -
l
in the receiver to produce even more accurate measurements,
since both the carrier frequency and the code rate are derived
coherently from the same reference frequency on-board the
satellite.
     The GPS C/A-code is 1023 bits long and is transmitted at
1.023Mbps. The C/A-code repetition period is therefore 1 ms.
The GLONASS C/A-code is 511 bits long and is transmitted at
511kbps, so it has the same repetition period as the GPS
C/A-code. The P-code is transmitted at 10 times the speed of
the C/A-code: 10.23Mbps for GPS and 5.11Mbps for GLONASS. The
transmitter power level for the P-code on L1 is 3dB below the
L1 C/A-code and the P-code on L2 is 6dB below the L1 C/A-code.
The P-code repetition period is very long, making an autonomous
search for synchronization unpractical. All P-code receivers
first acquire lock on the C/A-transmission, which also carries
information that allows a quick P-code lock.
     Both C/A- and P-codes are generated by digital
shift-registers with the feedback selected to obtain
pseudo-random codes. The navigation data is modulo-2 added to
the pseudo-random codes. Since the navigation-data rate is
very low, only 50bps, it does not affect significantly the
randomness properties of the codes used. The navigation data
at 50bps is synchronized to the C/A-code period to resolve the
timing ambiguity caused by the relatively short 1 ms C/A-code
repetition period.
     GPS "Block II" satellites may encrypt the published
P-code into the secret Y-code. This process is called
"Anti-Spoofing" (AS). Its purpose is to prevent an enemy from
jamming the GPS with false GPS-like signals. Details of the
GLONASS P-code are not published. In fact, the GLONASS P-code
is even not mentioned in [6], although these transmissions
can be easily observed on a spectrum analyzer.
     The GPS and GLONASS RF channel carrier frequencies are
shown on Fig. 7. All GPS satellites transmit on the same L1
and L2 carrier frequencies: 1575.42MHz and 1227.6MHz, which
are held in the exact ratio 77/60 and are integer multiples of
the fundamental GPS clock frequency of 10.23Mhz.
     Every GPS satellite transmits its own set of C/A- and
P-codes that have good cross-correlation properties with the
codes used by other GPS satellites. Since a GPS receiving
antenna is omnidirectional and receives many satellites at the
same time, the receiver is using Code-Division Multiple Access
(CDMA) techniques to separate signals coming from different
satellites. GPS satellites are therefore identified by the
Pseudo-Random-Noise code number (PRN#).
     The GLONASS satellites use 25 different RF channels.
Channel 0 is reserved for testing spare satellites while
channels 1 to 24 are dedicated to operational GLONASS
satellites. All GLONASS satellites transmit the same C/A-code
and are usually identified by the CHannel Number (CHN#).
The L1 and L2 carrier frequencies are in the exact ratio 9/7
and the channel spacing is 562.5kHz at L1 and 437.5kHz at L2.
     Although there exsist civilian P-code receivers, the
majority of civilian GPS or GLONASS receivers are C/A-only
receivers. Since the advantages of using the P-code are
limited, especially with SA, AS or both active, only the
C/A-code transmission will be discussed in detail here.





l- 12 -
l
2.6. GPS C/A-transmission format
--------------------------------
     GPS satellites use code-division multiplexing on both
C/A- and P-transmissions. Since C/A-codes are relatively short
sequences (only 1023 bits), the codes have to be carefully
selected for good cross-correlation properties. GPS C/A-codes
are Gold codes (named after their inventor Robert Gold) that
can be generated as a modulo-2 sum of two maximum-length
shift-register sequences.
     The GPS C/A-code generator is shown on Fig. 8. It
includes two 10-bit shift registers G1 and G2, both clocked
at 1.023MHz, each with a separate feedback network made of
exclusive-or gates. Both feedback networks are selected so
that both generated sequences have the maximal length of 1023
bits. Both shift registers are started in the "all-ones" state
and since both sequences have the same length, the shift
registers maintain the synchronization throughout the
operation of the circuit.
     Gold codes are obtained by a modulo-2 sum (another
exclusive-or operation) of the outputs of the two shift
registers G1 and G2. Different codes can be obtained by
changing the relative phase of the two shift registers.
Instead of resynchronizing the shift registers it is easier to
delay the output of one of them (G2). This variable delay is
acheived with yet another modulo-2 sum (exclusive-or) of two
G2 register taps. Exclusive-or feedback shift-regiter
sequences have the property that a modulo-2 addition of a
sequence with its delayed replica produces the same sequence,
but delayed by a different number of clocks.
     Choosing two G2 register taps, 45 different delays can
be generated yielding 45 different Gold codes with good
auto-correlation and cross-correlation properties. Out of
these 45 possible codes, 32 are allocated to GPS satellites
as shown on Fig. 9. The cross-correlation proprties of GPS
C/A-codes guarantee a crosstalk smaller than -21.6dB between
the desired and undesired satellite signals.
     The 50bps navigation data stream is synchronized with the
C/A-code generator so that bit transitions coincide with the
"all-ones" state of both shift registers G1 and G2. At 50bps
one data bit corresponds to 20 C/A-code periods.
     The navigation data is formatted into words, subframes
and frames. Words are 30 bits long including 24 data bits and
6 parity bits computed over the 24 data bits and the last two
bits of the previous word. Parity bits are used to check the
received data for errors and to resolve the polarity ambiguity
of the BPSK demodulator. 10 words (300 bits) form a subframe
which always includes a subframe sync pattern "10001011" and
a time code called "Time-Of-Week" (TOW). One subframe is
transmitted every 6 seconds.
     Five subframes form one frame (1500 bits) that contains
all of the information required to use the navigation signals.
One frame is transmitted every 30 seconds. The first subframe
in the frame contains the on-board clock data: offset,
drift etc. The second and third subframes contain the
precision ephemeris data in the form of keplerian elements
with several correction coefficients to accurately describe
the satellite's orbit. Finally, the fourth and fifth subframes
contain almanac data that is not required immediately and
are subcommutated in 25 consecutive frames, so that the whole



l- 13 -
l
almanac is transmitted in 12.5 minutes.
     The allocation of the single data words is completely
described in [5]. Most numerical parameters are 8-, 16-,
24- or 32-bit integers, either unsigned or signed in the
two's complement format. Angular values that can range from
0 to 360 degrees are usually expressed in semi-circles to
make better use of the available bits.
     GPS is also using its own time scale. The units are
seconds and weeks. One week has 604800 seconds and the week
count is incremented between Saturday and Sunday. GPS time
starts on the midnight of January 5/6, 1980. GPS time is a
continuous time and therefore it differs by an integer number
of leap seconds from UTC. The difference between UTC and GPS
time is included in the almanac message.

2.7. GLONASS C/A-transmission format
------------------------------------
     GLONASS satellites use the more conventional
frequency-division multiplexing at least for the C/A-code
transmissions. All GLONASS satellites use the same C/A-code,
generated by a 9-bit shift register G as shown on Fig. 10.
The GLONASS C/A-code is a maximum-length sequence and thus
has an ideal auto-correlation function.
     Frequency-division multiplexing allows a better channel
separation than code-division multiplexing. The separation
between two adjacent GLONASS channels should be better than
-48dB. A large channel separation is useful when the signal
from one satellite is much weaker because of reflected waves
and/or holes in the receiving antenna radiation pattern.
On the other hand, the GLONASS satellites require a wider RF
spectrum and a GLONASS C/A-receiver is necessarily more
complex than a GPS C/A-receiver.
     The GLONASS navigation data stream is synchronized with
the C/A-code generator so that level transitions coincide
with the "all-ones" state of the shift register. The
navigation data stream is formatted into lines of the duration
of 2 seconds. Each line contains 85 information bits,
transmitted at 50bps for 1.7 seconds and a "time mark" sync
pattern "111110001101110101000010010110", which is a
pseudo-random sequence of 30 bits transmitted at 100bps for
the remaining 0.3 seconds.
     The 85 information data bits always start with a leading
"0", followed by 76 bits containing navigation information
and 8 parity-checking bits, computed according to the (85, 77)
Hamming code. After computing the parity bits, all of the
85 bits are differentially encoded to resolve the phase
ambiguity in the receiver. Finally, the 85 differentially-
-encoded bits are manchester encoded, so that a "10" pattern
corresponds to a logical "one" and a "01" pattern corresponds
to a logical "zero". The additional transition in the middle
of the data bits introduced by the manchester encoding
speeds-up the synchronization of the receiver.
     15 navigation data lines form one frame of the duration
of 30 seconds. The allocation of the single data bits in the
frame is completely described in [6]. The first four lines
of a frame contain the time code, on-board clock offset and
drift and precision ephemeris data of the satellite orbit in
the form of a state vector (position vector and velocity
vector). To simplify the computations in the user's receiver,



l- 14 -
l
the corrections for the Sun- and Moon-gravity forces are
also supplied.
     The almanac data is transmitted in the remaining 11 lines
of the frame. Almanac satellite ephemeris is in the form of
keplerian elements and is transmitted in two consecutive lines
in a frame. The whole almanac is transmitted in five
consecutive frames also called a superframe of the duration of
2.5 minutes. The various numerical parameters are transmitted
as different size, either unsigned or signed integers. Signed
integers are transmitted in the form of a sign bit followed
by an usigned integer representing the absolute value of the
number (this is different from the two's complement notation!)
Angular values are usually expressed in semi-circles.
     The GLONASS time is kept synchronized to UTC. GLONASS
uses more conventional time units like days, hours, minutes
and seconds. The day count begins with a leap year (currently
1992) and counts up to 1461 days before returning back to
zero.












































l- 15 -
l
3. GPS & GLONASS receiver theory of operation
=============================================

3.1. GPS/GLONASS receiver operation principles
----------------------------------------------
     Since the signals transmitted by GPS and GLONASS
satellites are similar, the receiver design for any of these
systems follows the same guidelines. The principle block
diagram of a GPS or GLONASS receiver is shown on Fig. 11.
Only a single channel receiver is shown for simplicity. The
problem of simultaneously receiving more than one signal (like
the C/A-signal and both P-signals from four or more satelites)
will be discussed later.
     Since the user's position, velocity and attitude are
unknown in a navigation problem, satellite navigation receivers
generally use either one or more omnidirectional antennas.
All satellite navigation signals are circularly polarized
(usually RHCP) to allow the user's receiver to further
attenuate any reflected waves, since circularly polarized
waves change their sense of polarization on each reflection.
Reflected waves are a major nuisance in precision navigation
systems: they represent an unpredictable propagation anomaly
which is a major source of measurement errors.
     The radio signals collected by an omnidirectional
receiving antenna are weak. A low-noise amplifier will prevent
any further degradation of the signal-to-noise ratio, but it
can not reduce the thermal noise collected by the antenna nor
unwanted navigation satellite transmissions on the same
frequency. GPS and GLONASS satellite signals are wideband,
ranging from 1MHz (GLONASS C/A-code) to 20MHz (GPS P-code),
and the satellite transmitter power is limited to around
25dBW EIRP (L1 C/A-code for both GPS and GLONASS) or even less
than this (P-transmissions), making the signal usually weaker
than the thermal noise collected by the antenna.
     Although buried in thermal noise and interferences, these
signals can still be used, since the given bandwidth and
megabits-per-second rates apply to a known code and not to
the information bandwidth, which is smaller than 1kHz for both
timing and Doppler-shift measurements and the navigation data
transmitted at 50bps. In other words, GPS and GLONASS signals
are direct-sequence spread-spectrum signals, using
Code-Division Multiple Access (CDMA) techniques [7].
     A GPS or GLONASS receiver will first downconvert the
signals to a suitable IF and amplify them before further
processing. At this stage a wide IF filter, corresponding to
the complete original signal bandwidth, can be used to improve
the dynamic range of the receiver. The downconverter may be
made tunable if widely separated channels are to be received,
like the GLONASS C/A-transmissions.
     The wideband IF signal is then multiplied by (mixed with)
a locally-generated satellite signal replica, modulated by
the same code. If the locally generated code is synchronized
to the satellite transmission, the bandwidth of the desired
mixing product will collapse down to almost zero, since two
identical 0/180-degrees BPSK modulation processes exactly
cancel each other. On the other hand, the bandwidth of all
unwanted signals, like noise or interferences, will be further
expanded by this operation to a double bandwidth.
     Since the bandwidth of the desired signal collapses, this



l- 16 -
l
operation is usually called signal spectrum despreading. The
desired signal can now be filtered-out with a narrow IF filter
having a bandwith ranging from 100Hz to 10kHz in a GPS or
GLONASS receiver. After the narrow IF filter, the
signal-to-noise ratio finally acheives useable values and
typically reaches 20dB.
     The filtered IF signal is then used for several purposes.
First, it is used to acquire and maintain synchronization of
the locally generated code. Dithering the locally-generated
code back and forth by a fraction of the bit period generates
an amplitude modulation on the filtered signal. The phase of
this modulation contains the information required to keep
the synchronization of the local code generator.
     The filtered IF signal is also fed to a BPSK demodulator
(usually a squaring PLL or a Costas PLL) to extract the 50bps
navigation message data. The BPSK demodulator also provides a
regenerated carrier that is used for Doppler-shift
measurements. On the other hand, the code-timing information
is obtained from the local code generator. All three signals,
code timing, Doppler shift and 50bps navigation data are fed
to the receiver CPU to compute the user position, velocity,
accurate time etc...
     For Earth-located, slowly-moving users, the Doppler
shift on the satellite signals is mainly due to the satellite
motion and amounts up to +/- 5kHz on the L1 frequency.
In most cases some fine tuning will be required to compensate
the Doppler shift in front of the narrow IF filter. Some
fine-tuning capability is also required to compensate the
local oscillator frequency drift. In GPS and GLONASS receivers
all of the required frequencies are obtained from a single
TCXO with a stability of a few parts per million. Since one
part per million is 1.6kHz at the L1 frequency, the frequency
uncertainty of the receiver is comparable in magnitude to the
expected Doppler shift.
     Like in all spread-spectrum systems, the initial code
sync acquisition is a critical operation in a GPS or GLONASS
receiver. Most receivers make an exhaustive search for
C/A-code synchronization. Testing a possible code phase
typically takes around 10 milliseconds each, so an exhaustive
search may take more than 10 seconds. This figure needs to
be multiplied by the number of frequencies tested, due to
an unknown Doppler shift or unpredictable TCXO drift.
     A "cold start" of a GPS or GLONASS receiver may therefore
take up to one hour, since the receiver does not know which
satellite (PRN# or CHN#) to look for nor the Doppler shift
nor the code phase. A "warm start" is much faster since
the receiver should know the almanac satellite ephemeris, the
approximate user location and the approximate time. From this
information one can get all visible satellites and compute
the corresponding Doppler shifts, so that the code phase and
the TCXO drift are the only unknowns left.
     The period of the P-code is far too long to make an
exhaustive sync search practical. All P-code receivers need
to acquire the C/A-code first, decode the navigation data
and synchronize their local P-code generator to the C/A-code
transmission first. Since the P-code rate is only 10 times
the C/A-code rate, there are very few possible P-code phases
left to be tested to lock on the P-transmission.
     GPS and GLONASS have been designed to supply timing



l- 17 -
l
codes, the user position being computed from the measured
propagation time differences. Additionally, the user velocity
can be computed from the already known position and the
measured Doppler-shift differences on the signal carriers.
Although the Doppler shift can also be measured on the code
rates, this measurement is usually very noisy. On the other
hand, no absolute delay difference can be measured on the
carrier, since the carrier phase becomes ambiguous after
360 degrees. Finally, relating the carrier phase to the code
phase may produce excellent results, but requires an accurate
compensation of ionospheric effects, which have opposite
signs: the ionosphere delays the modulation and at the same
time advances the carrier phase!
     Besides the described principle of operation of a GPS
or GLONASS receiver, there are some other possibilities.
For example, the C/A-code sync could be obtained much faster
using an analog (SAW) or digital (FFT) correlator.
To evaluate ionospheric errors, codeless reception techniques
can be used to receive both P-transmissions on L1 and L2
frequencies without even knowing the codes used.

3.2. Digital Signal Processing (DSP) in GPS/GLONASS receivers
-------------------------------------------------------------
     After the principles of operation and the required
functions of an electronic circuit are known, one has to
decide about the technology to practically implement the
circuit. In most cases GPS or GLONASS receivers are mobile
units installed on vehicles or even portable handheld units.
The receiver weight, size and power consumption are all
important. While every GPS or GLONASS receiver must have an
antenna, a RF front-end and a digital computer to solve the
navigation equations, the IF signal processing may include
just a single channel in a simple C/A-only receiver or more
than 10 channels in a full-spec L1 & L2 P-code receiver.
     When the same circuit function needs to be duplicated
several times, like the IF processing channels in a
radio-navigation receiver, it is usually convenient to use
Digital Signal Processing (DSP) techniques. An important
advantage of DSP over analog circuits is that duplicated
channels are completely identical and require no tuning or
calibration to accurately measure the difference in the
time of arrival or Doppler shift of radio-navigation signals.
A single DSP circuit can also be easily multiplexed among
several signals, since the internal variables of a DSP circuit
like a PLL VCO frequency or phase can be stored in a computer
memory and recalled and updated when needed again.
     The bandwidth of the navigation satellite signals is
several MHz and this is a rather large figure for DSP.
Implementing the whole IF signal processing of a GPS/GLONASS
receiver completely in software (like described in the
introduction to DSP techniques in [8]) is difficult although
it has been done [9] for the GPS C/A-code using powerful
microcomputers. Most GPS/GLONASS receivers use a combination
of dedicated DSP hardware and software for IF signal
processing. Dedicated DSP hardware is only used where the
the bandwidth is large and the functions are relatively
simple, like the local satellite signal replica generation and
the signal despreading, while all other functions, including
all feedback loops, are implemented in software.



l- 18 -
l
     When designing a DSP circuit and in particular when
designing dedicated DSP hardware it is essential to know,
besides the signal bandwidth or sampling frequency, also the
resolution or number of bits per sample required to represent
the signals involved [10]. A GPS or GLONASS signal is a
constant amplitude signal and limiting is therefore not
harmful. However, after the wide IF filter in the receiver
there is a mix of many satellite signals of different strength
and lots of thermal noise as well. If such a mix of signals is
limited, the resulting intermodulation distortion degrades the
signal-to-noise ratio by around 2dB.
     Since navigation satellite signals are pseudo-random
sequences, all undesired signals and all intermodulation
products only affect the desired signal in the same way as
thermal noise. Therefore, in a GPS/GLONASS receiver, very few
bits are required to represent the wideband IF signal. Most
GPS/GLONASS receivers simply limit the wideband IF signal,
thus accepting the 2dB sensitivity degradation and
representing each sample with just two quantization levels
or one single bit. Increasing the number of bits per sample
only increases the DSP hardware complexity while bringing
marginal sensitivity improvements, so that no known receiver
design uses more than 3 bits per sample (8-level
quantization).
     On the other hand, an 1-bit/sample DSP GPS/GLONASS
receiver may have a really simple IF signal processing as
shown on the principle block diagram on Fig. 12. The IF signal
is limited, so no AGC is required. Signal sampling and A/D
conversion is performed by a single D-flip-flop. Signal
despreading or multiplication with the locally generated
signal replica is accomplished with an exclusive-or gate.
Since the narrow IF can be selected close to zero, the narrow
IF bandpass filter may be replaced by a lowpass filter or
an integrator. In the case of 1-bit samples, the latter is
simply a counter with the clock set to the sample rate and
gated by the input signal.
     However, after the narrow IF filtering the resulting
signal can no longer be represented with a single bit per
sample, if the sample rate of the narrowband signal is
significantly reduced. In a C/A-code receiver, the integrator
is read and then reset each millisecond, to match the period
of either GPS or GLONASS C/A-codes, since the auto- and
cross-correlation properties of these codes are only
maintained over an integer number of code periods. An
integration period of 1ms corresponds to a narrow IF bandwidth
of +/- 500Hz around the center frequency. The latter is a very
good choice for a GPS or GLONASS receiver.
     Any further signal processing after the integration can
be conveniently performed in software, since an interrupt rate
of only 1kHz can be accepted by any microprocessor. The
accumulated data in the integrator has a resolution of
12 to 14 bits, so any further software processing can be done
without any loss of quantization accuracy nor processing speed
of a general-purpose 16-bit microprocessor.
     Dedicated hardware is also required for the generation of
the local signal replica. Carriers or rates are conveniently
generated in Numerically Controlled Oscillators (NCOs).
A NCO includes a digital adder and an accumulator. In every
clock cycle, a constant representing the desired output



l- 19 -
l
frequency or rate is added to the accumulator. If an analog
output were desired, the accumulator content could be fed to
a ROM containing a sine table and then to a D/A converter,
forming a direct digital frequency synthesizer.
     In a 1-bit DSP navigation-receiver the sine table and
D/A converter are not required. Since the DSP hardware
operates with 1-bit data, it is sufficient to take the MSB
of the NCO accumulator as the frequency output. Two NCOs are
required: on for the carrier frequency and another for the
code rate. The code-rate NCO supplies the clock to a code
generator like the ones shown on Fig. 8 or 10. The output
of the code generator is exclusive-or gated with the output
of the carrier NCO to produce a BPSK-modulated satellite
signal replica.
     Of course both NCOs have to be accurately steered to the
required frequency and phase to maintain lock on the incoming
signal. The feedback function can be performed by the
microprocessor, since the feedback speed is very low: a 100Hz
update rate is usually fast enough. Finally, the NCO frequency
can be easily steered modifying the addition constant and the
NCO phase can be easily steered modifying the accumulator
content. In a time-multiplexed IF channel, both can be easily
stored by the microprocessor and recalled when the channel
hardware is switched back to the same satellite signal.
     From the technology point of view, a DSP IF channel can
be built on an "Eurocard" size printed circuit board using
just bare 74HCxxx logic. A single IF channel may also be
programmed in a programmable-logic integrated circuit.
Finally, the complete IF signal processing with 6 or 8
independent channels may be integrated in a single custom
integrated circuit. Commercial satellite navigation receivers
use custom integrated circuits essentially to prevent
unauthorized duplication. On the other hand, bare 74HCxxx
logic is preferred for an amateur, homemade receiver.
Hopefully programmable-logic ICs will some day become
standardized and the necessary programming tools cheap enough
to allow amateur applications.

3.3. Multi-channel reception of navigation signals
--------------------------------------------------
     A satellite navigation receiver should be able to
receive the signals from four or more satelites at the same
time, to be able to measure time and Doppler differences.
When the GPS specifications were published back in 1975 [4],
the digital computer was the largest and most complex part of
a satellite navigation receiver. Both GPS and GLONASS
receivers were initially intended to have several analog
IF processing channels, one per each signal type per
satellite. Since these receivers were intended for military
vehicles like fighter aircrafts, tanks or battle ships,
the price and complexity of several analog IF processing
channels was almost unimportant.
     Early civilian GPS receivers also used analog IF
processing, although initially limited to the C/A-code and
one or two time-multiplexed IF channels. Time-multiplexing
is difficult with analog IF channels, since the latter have
to reacquire lock each time the satellites are changed.
Lock acquisition may take 15 to 20 seconds, so that the
measurement loop through four or more satellites takes



l- 20 -
l
several minutes. These receivers were only suitable for
stationary or slowly-moving users.
     The introduction of DSP techniques and inexpensive
computers allowed much faster multiplexing. Since the
variables of a DSP circuit can be stored and recalled, a DSP
IF channel does not need to reacquire lock each time it is
switched to another satellite signal. A DSP IF channel is
typically switched among satellite signals around a hundred
times per second making the whole loop among all required
signals a few ten times per second. However, because of the
available signal-to-noise ratio, the navigation solution in a
C/A-code receiver only needs to be computed about once per
second.
     All current commercial GPS and GLONASS receivers use
DSP IF processing. Small handheld C/A-code receivers have one,
two or three time-multiplexed IF channels. Mobile C/A-code
receivers have 5, 6 or even 8 independent channels so that
no multiplexing is required. Time multiplexing makes the
carrier lock and Doppler measurements difficult and
unreliable, so it is undesired in mobile receivers.
     Unfortunately, multi-channel GLONASS receivers require a
wider raw signal IF and a much higher sampling rate due to
the wide FDMA channel spacing. On the other hand, GPS
receivers require the same raw IF bandwidth regardless of the
number of channels thanks to CDMA. The higher sampling rates
required for GLONASS are a little unpractical with currently
available integrated circuits. Maybe this is another reason
why GPS receivers are more popular and GLONASS is almost
unknown. Since faster ICs will certainly be available in
the future, one can expect that combined GPS/GLONASS
receivers will become standard.
     In this article I am going to describe a single-channel
C/A-only receiver using fast time multiplexing. This receiver
can be built in two versions: GPS or GLONASS. Although both
versions use the same modules as much as possible, this is
not a combined GPS/GLONASS receiver yet. The main limitation
of a single IF channel, time-multiplexed receiver is that the
maximum number of simultaneously tracked satellites is limited
to four or five, so that a combined GPS/GLONASS receiver does
not make much sense.

3.4. Practical GPS receiver design
----------------------------------
     The block diagram of the described GPS receiver is shown
on Fig. 13. In the microwave frequency range, at L-band, the
antenna needs a direct visibility of the satellites. Therefore
it has to be installed outdoor, on the vehicle roof or on top
of a portable receiver. Due to its excellent performance, a
half-turn quadrifilar helix is used as a circularly polarized,
hemispherical-coverage antenna. The LNA is installed directly
under the antenna. Using two inexpensive GaAs FETs it acheives
30dB of gain making any following (reasonable) cable loss
almost unimportant.
     The GPS receiver includes a fixed-tuned downconverter to
a suitable IF, an IF amplifier and limiter, a dedicated DSP
hardware, a MC68010 based microcomputer with a small keyboard
and a LCD display and a single master crystal oscillator for
all frequency conversions and sampling rates. The
downconversion from the GPS L1 frequency (1575.42MHz) is made



l- 21 -
l
in two steps for convenient image filtering. The first wide IF
is in the 102MHz range and the second wide IF is in the 10MHz
range. The wide IF bandwidth is set to around 2MHz. The actual
value of the wide IF bandwidth is not critical, since filtering
is only required to prevent spectrum aliasing in the signal
sampling circuit.
     6139kHz was selected as master crystal oscillator
frequency of the described GPS receiver, since the best TCXOs
are usually available for the frequency range between 5MHz
and 10MHz. The output of the 6139kHz master oscillator is
used both as the sampling frequency for the IF A/D conversion
and as an input to a chain of multiplier stages to supply all
of the frequencies required in the downconverter. Limiting
the temperature range from 0 to 30 degrees C, as encountered
during normal receiver operation, the TCXO was replaced by a
much less expensive conventional crystal oscillator in all of
the prototypes built.
     Sampling the 10MHz wide IF signal with 6139kHz produces
a third downconversion to a 2303kHz nominal center frequency.
The latter is the final carrier frequency that needs to be
regenerated in the dedicated DSP hardware. The dedicated DSP
hardware is designed as a microprocessor peripheral with
read and write registers and is interrupting the MC68010
CPU once every millisecond to match the GPS C/A-code period.
     In the portable, stand-alone GPS receiver, the
operating software is stored in a compressed form in a
32kbytes EPROM. After power-on reset, the software is
decompressed in 128kbytes of battery-backed CMOS RAM, which
is also used to store the system almanac and other data to
speed-up the acquisition of four valid satellites. For the
same reason the CPU also has access to a small battery-backed
real-time clock chip.
     A small 8-key keyboard is used to select the various
menus of the operating software and manually set some receiver
parameters if so desired. The portable version of the GPS
receiver is using a LCD module with integrated driving
electronics and two rows of 40 alphanumeric (ASCII) characters
each, to display the receiver status, the almanac data or
the results of the navigation computations.

3.5. Practical GLONASS receiver design
--------------------------------------
     The block diagram of the described GLONASS receiver is
shown on Fig. 14. The GLONASS receiver uses the same type of
antenna and LNA and the same dedicated DSP hardware and
microcomputer as its GPS counterpart. The main difference
between the two receivers is in the downconverter. The GLONASS
receiver includes a tunable downconverter, otherwise the wide
FDMA channel spacing would require unpractically high sampling
rates in the dedicated DSP hardware.
     The downconversion from the GLONASS L1 frequency range
(1602 to 1615.5MHz) is made in two steps for convenient image
filtering. To reduce group-delay variations, the first
conversion is made tunable and the second is fixed. In this
case the only contribution to group-delay variations across
the GLONASS L1 frequency range are the tuned circuits at
1.6GHz. Group-delay variations introduce errors in the
measured time differences, so they immediately affect the
accuracy of a navigation receiver. This problem does not



l- 22 -
l
exsist in a GPS receiver, since all GPS satellites transmit
on the same carrier frequency and any signal filtering
produces the same group delay on all satellite signals that
exactly cancels-out when computing the differences.
     Both wide IFs are fixed tuned at 118.7MHz and 10.7MHz
respectively. To avoid any group-delay variations in the
wide IFs, the frequency synthesizer steps must accurately
match the channel spacing so that all signals are converted
to the same IF values. Finally, the IF limiter should not
introduce a variable delay as the input signal strength is
changed when switching among channels. The second wide IF
signal at 10.7MHz is sampled with 4500kHz producing a third
downconversion to a nominal center frequency of 1687.5kHz.
     There are several difficult-to-meet requirements for
the frequency synthesizer supplying the signal for the first
conversion. This synthesizer has to provide a clean signal
in the frequency range from 1483 to 1497MHz in steps of
562.5kHz. Its phase noise should be low enough to allow
carrier lock and 50bps navigation data demodulation: its
spectral linewidth should be about 10 times narrower than
required in a voice SSB receiver. Finally, in a
time-multiplexed, single-channel receiver the synthesizer
should be able to switch and settle to another frequency in
less than 1ms, the GLONASS C/A-code period, to avoid
increasing the switching dead time.
     The frequency synthesizer is a PLL with a frequency
converter in the feedback loop, to decrement the divider
modulo, increase the loop gain, speed-up the settling and
improve the output phase noise performance. The feedback
signal is downconverted to the frequency range 25 to 38MHz,
so that a very low programmable loop-divider modulo
between 45 and 69 is required. The comparison frequency is
set to 562.5kHz. A well-designed PLL will settle in
100 to 200 clock periods of the comparison frequency and the
described PLL acheives this performance with a settling time
between 200 and 300 microseconds.
     The described GLONASS receiver is using a master crystal
oscillator at 18.000MHz. This frequency is multiplied by 6
to obtain the 108MHz signal required for the second conversion
and by 81 to obtain the 1458MHz signal required for the PLL
feedback-loop conversion. The master oscillator frequency is
divided by 4 to obtain the 4500kHz sampling frequency and
by 32 to obtain the 562.5kHz PLL reference frequency.
Like in the GPS receiver, in place of an expensive TCXO
conventional crystal oscillators were used in all of the
prototypes built, limiting somewhat the operating temperature
range.
     In the described GLONASS receiver, the microcomputer
has one function more. Besides controlling the dedicated DSP
hardware, keyboard and LCD display, all identical to the GPS
counterparts, the microcomputer has to set the frequency
synthesizer when switching among channels. The operating
software is very similar to that in the GPS receiver and has
the same hardware requirements: 32kbytes of EPROM, 128kbytes
of battery-backed CMOS RAM and a battery-backed real-time
clock.






l- 23 -
l
3.6. GPS/GLONASS dedicated DSP hardware design
----------------------------------------------
     Although the theory of operation of an 1-bit DSP GPS or
GLONASS receiver has already been discussed, the practical
implementation still offers many different choices and
some additional problems to be solved. For example, from the
theoretical point-of-view it is unimportant whether the
code lock or the carrier lock is acheived first. In practice,
the code lock should be acheived first and should be
completely independent from the carrier lock, both to speed-up
the initial signal acquisition and to avoid loosing lock at
short signal dropouts (obstructions, fading) or receiver
frequency reference instabilities.
     The block diagram of the practically implemented
GPS/GLONASS dedicated DSP hardware is shown on Fig. 15.
Although the implemented hardware is intended for a single
channel, time multiplexed operation, it differs significantly
from the theoretical block diagram shown on Fig. 12. The main
difference is that there are four signal-despreading mixers
(multipliers, ex-or gates) and four integrators (counters) for
one single channel.
     In practice, two separate signal-despreading mixers are
required when downconverting to a narrow IF of almost zero.
The mixers are driven with the same satellite signal replica,
modulated with the same code, but with the carriers in
quadrature. In this way no information is lost after signal
despreading, downconversion and integration. The code lock
can be made completely independent from the carrier lock,
since the narrow IF signal amplitude can be computed out of
the I and Q integration sums without knowing the carrier
phase. The same I and Q integration sums are used in a
different way to acheive carrier lock and extract the 50bps
navigation data. Due to the low sample rate (1kHz) the latter
are conveniently performed in software.
     Although code lock may be maintained by dithering the
locally generated signal replica, two separate narrow IFs
for an "early" and a "late" local signal replica provide a 3dB
improvement in the signal-to-noise ratio on time-delay
measurements. The former solution, code dithering, is usually
used in receivers with an analog narrow IF, since it is
difficult to build two identical circuits in analog technology.
The latter solution is used in receivers with a DSP narrow IF,
since DSP circuits perform the same numerical operations and
are therefore mathematically identical.
     To acheive the 3dB signal-to-noise improvement, two
separate sets of I and Q signal-processing chains for the
"early" and "late" signal replicas need to be used. This
brings the total number of signal-despreading mixers and
integrators to four. Of course the local signal replica
generation includes the generation of four different signals:
I-EARLY, Q-EARLY, I-LATE and Q-LATE. All these signals can
be obtained from a single carrier and code generator, since
they are merely delayed versions of the same signal: either
the carrier or the code or both are delayed. In DSP, delays
can be easily obtained with shift registers.
     On the other hand, the local satellite signal replica
generation can be simplified with a look-up table. Since
the integration period is 1ms and the input sample rate is
6139kHz (GPS) or 4500kHz (GLONASS), there are only 6139 or



l- 24 -
l
4500 different bits to be stored in the look-up table for
each despreading mixer and integrator. The look-up table
is written by the microcomputer since it does not need to
be updated very frequently.
     The carrier frequency only needs to be updated less than
once per minute while the carrier phase can be adjusted in
software since both I and Q integration sums are available.
The code rate does not need to be adjustable if the code phase
can be corrected every 10 milliseconds. For the latter reason
the code phase is made adjustable in hardware by a
variable-delay circuit.
     The variable-delay circuit used to adjust the code phase
also brings a disadvantage. The carrier frequency can only be
adjusted in steps of 1kHz, since the carrier phase should be
continuous when the address counter reaches the end of the
look-up table and is reset back to the beginning. The carrier
frequency error can therefore reach +/- 500Hz and although
it is compensated in software, it degrades the sensitivity
of the receiver by up to 4dB (at +/- 500Hz error).
     There are several ways to avoid this problem, like two
separated code and carrier look-up tables or a double-length
table with a presettable address counter. However, in
practice the simpliest circuit was preferred in spite of the
4dB sensitivity penalty. Both GPS and GLONASS receiver
prototypes are therefore using the simple look-up table
generator described above.
     The local signal replica generation also explains the
choice of the input sampling rates and wide IF nominal center
frequencies. Ideally, to avoid spectrum aliasing the wide IF
nominal center frequency should be equal to 1/4 of the sampling
rate or any odd multiple of this value: 1536kHz for GPS or
1125kHz for GLONASS.
     In practice 6139kHz was selected as the sampling rate for
the GPS receiver to avoid interferences with the GPS C/A-code
rate (1023kHz), since the described look-up table generator
maintains a fixed phase relationship between the code
transitions and sampling rate. Considering the various
conversion frequencies obtained from the same source, an IF
of 2303kHz resulted after signal sampling.
     In the GLONASS receiver, any interferences between the
sampling rate and code rate are unimportant since all
satellites use the same C/A-code. The sampling rate of 4500kHz
was chosen for convenience. Considering the operation of the
frequency synthesizer, the final wide IF value could be chosen
in 562.5kHz steps. The value of 1687.5kHz was selected to
avoid some spurious frequencies generated in the synthesizer.
     Finally, the described dedicated DSP hardware always
requires the support of a microcomputer. The latter should
compute and load the look-up tables first. After each
interrupt request (every millisecond) the microcomputer
reads all four integrated sums. From the I and Q components
it computes the early and late magnitudes used to search and
maintain code lock. The code phase required to maintain lock
is at the same time the result of a time-delay measurement,
referenced to the receiver clock. The difference of two
such measurements is a parameter of a navigation equation.
     On the other hand, the I average and Q average are
supplied to a Costas-loop demodulator to recover the carrier
and demodulate the 50bps navigation data bits. Then the



l- 25 -
l
subframe or line sync is detected to format the data stream
and check the parity bits before the navigation data is used
in the computations.



























































l- 26 -
l
4. Homemade receiver modules for GPS & GLONASS
==============================================

4.1. Quadrifilar backfire helix antenna
---------------------------------------
     Although long range, precision navigation systems like
GPS or GLONASS were designed to be independent as much as
possible of the performance of either transmitting or
receiving antennas, the antennas used still have some
influence on the system performance. The transmitting antennas
installed on the spacecrafts have a shaped beam to supply any
Earth-located user with the same signal strength and use the
on-board transmitter power more efficiently. Maintaining the
same signal strength is especially important in CDMA, since
the GPS C/A-codes are too short to offer a very good crosstalk
performance.
     The ideal receiving antenna should have a hemispherical
radiation pattern, offering the same signal strength from
a satellite at zenith and from another satellite just above
horizon. Further, the receiving antenna should match the
transmitter polarization (RHCP) in all valid directions.
Finally, the receiving antenna should attenuate any signals
coming from undesired directions, like signals coming from
negative elevations, since these are certainly reflected
waves and the latter are a major source of measurement errors
due to their unknown propagation path.
     Although a turnstile antenna (two crossed dipoles fed in
quadrature) with or without a reflector is frequently used for
satellite reception, this antenna is not very suitable for
satellite navigation for several reasons. The polarization of
a turnstile antenna is circular only in the zenith direction
and is completely linear in the horizon plane. Therefore, a
turnstile antenna offers no discrimination between the desired
RHCP direct wave and the unwanted LHCP reflected wave, since
circularly polarized waves change their sense of polarization
on each reflection. Reflected waves cause severe measurement
errors and a relatively slow and deep signal fading, so that
the receiver even looses lock on the signal.
     A better alternative is a microstrip patch antenna.
A single microstrip patch resonator provides a useful
radiation pattern with a reasonably circular polarisation over
a wide range of elevations. Unfortunately the radiation
pattern of a microstrip antenna falls down to zero in the
horizon plane. Microstrip antennas are usually used when
a simple, low-profile antenna is required, usually to be
installed on a vehicle roof. Since low-elevation satellites
can not be received, a microstrip antenna usually limits the
available GDOP.
     The best antenna for satellite navigation and other
applications requiring hemispherical coverage seems to be the
quadrifilar backfire helix (also called a "volute" antenna).
Such an antenna provides a shaped conical beam. The beam
shaping and cone aperture can be controlled by adjusting the
helix radius, turns pitch distance and number of turns as
described in [11]. By the way, the same type of antenna is
frequently used on low-Earth orbit satellites, like the NOAA
weather satellites.
     As the GPS and GLONASS satellites already provide a
constant signal strength for Earth-located users regardless



l- 27 -
l
of the satellite elevation, no particular beam shaping is
required for the receiving antenna. The optimum number of
turns of a quadrifilar backfire helix used as a GPS or GLONASS
receiving antenna seems to be between 1.5 and 3. Making a
quadrifilar backfire helix longer by increasing the number of
turns does not have much effect on the gain or the beam-cone
aperture, but it improves the beam shaping and further
attenuates the undesired lobe in the opposite direction
(downwards).
     Although the best GPS receivers use such a quadrifilar
helix with 1.5 or 2 turns, such an antenna is difficult to
manufacture and test. In particular, the four helical wires
have to be fed in quadrature and there is very little space
on top of such an antenna to install the feeding network.
Further, a 2-turn backfire helix is rather large (20cm high)
for a portable receiver. If its improved pattern performance
is to be fully exploited, the direction of its axis should
not deviate too much from vertical and this is not a very
practical requirement for a portable receiver.
     Most GPS/GLONASS receivers therefore use a simplier
antenna, usually a short one-half turn backfire helix like
shown on Fig. 16. Making the quadrifilar helix shorter
resonance effects can be used to feed the four helical
wires with the proper signal phases. In particular, one pair
of wires is made shorter to make its impedance capacitive
at the operating frequency and the other pair of wires is made
longer to make its impedance inductive at the operating
frequency.
     To obtain RHCP a conventional end-fire helix has to be
wound like a right-hand screw. The backfire helix is just
opposite: to obtain RHCP the backfire helix has to be wound
as a left-hand screw, besides the proper phasing of the four
helical wires, of course! Further, the backfire helix
requires no reflector. The four helical wires are fed at one
end of the helix and shorted together at the other end of the
helix. Since the main (desired) radiation lobe is directed
towards the feedpiont and away from the shorted end, such an
antenna is called a backfire antenna.
     The feedpoint impedance is in the 50ohm range,
symmetrical. A good match to 50ohms is usually sacrified for
the radiation pattern which is much more important.
Usually one of the four helical wires is replaced by a
semi-rigid coaxial cable of the same outer diameter to form
an "infinite balun". On the other hand, the performance of the
antenna is not degraded much if no balun is used like shown
on Fig. 16.
     In the practical construction of a half-turn quadrifilar
helix it is especially important to respect the exact lengths
of the helical wires, since the antenna uses resonance effects
and is rather narrowband. The dimensions shown on Fig. 16 are
for the GPS L1 frequency (1575.42MHz). A GLONASS L1 antenna
should be approximately 3% smaller. Finally, an antenna for
both GPS and GLONASS L1 channels can be built by designing it
for the average of the two frequency bands.








l- 28 -
l
4.2. Low-noise amplifier
------------------------
     In all satellite microwave receivers it is usual to
install a low-noise amplifier close to the antenna to avoid
any feedline losses and make use of the very low sky noise
temeprature in the microwave frequency bands. A GPS or GLONASS
navigation receiver does not require a particularly low-noise
antenna amplifier since the omnidirectional antenna collects
lots of ground noise (300K) and the systems themselves were
designed with large margins allowing a receiver noise figure of
5dB or even more. Using a better antenna amplifier can only
bring marginal improvements.
     A two-stage GaAs FET antenna amplifier [12] was initially
developed for a GPS receiver. This amplifier is using lumped
components (coils) for input, interstage and output matching
(see the circuit diagram on Fig. 17) and is constructed in
free air to minimize any matching circuit losses (see the
layout on Fig. 18). Further, this amplifier circuit design
provides stable operation even with highly resonant sources
like the described quadrifilar helix antenna and in practice
the circuit resulted easily reproducible.
     The antenna amplifier is built inside a small metal
case with the dimensions of 50mm(length)X20mm(width)X
X15mm(height) with BNC connectors for both input and output.
Since the supply voltage of +12V is fed through the output
connector, care must be exercised not to swap the two
connectors in practical use! On the other hand, the suggested
preamplifier case is small enough to avoid resonance problems
with ordinary GaAs FETs, like the MGF1302. However, if higher
gain devices or HEMTS like CFY65 are used in this amplifier
design, a small piece of absorber foam is usually required to
avoid oscillations at very high frequencies. To avoid any
additional losses at 1.5GHz, the absorber should be placed
just under the cover and only above the second stage.
     The described preamplifier is a wideband device and does
not require any particular tuning. The only adjustments
necessary are the source resistors of both GaAsFETs to obtain
a suitable DC bias for both stages.
     The gain of the described antenna amplifier is, depending
on the devices used, somewhere between 25dB and 35dB. This is
enough to compensate for the losses in up to 10m of RG-214
cable and the much higher noise figure of the downconverter.
Since GPS or GLONASS receivers are usually used as portable
equipment, the antenna and preamplifier are installed directly
on the top of the receiver.

4.3. GPS RF module
------------------
     The GPS receiver only requires a single-frequency
(1575.42MHz) downconverter and its design is relatevely
straightforward. The GPS downconverter includes two modules:
a RF module built in microstrip technology and an IF strip
built on a simple, single-sided printed circuit board.
     The circuit diagram of the GPS RF module is shown on
Fig. 19. The GPS RF module includes three RF amplifier stages
and the first downconversion mixer. The amplifier stages are
identical and use silicon MRF571 transistors. Much of the gain
provided by these transistors is lost in the microstrip
filters, since the latter are etched on a lossy but inexpensive



l- 29 -
l
glassfiber-epoxy laminate.
     The first downconversion to 102MHz is performed by a
harmonic mixer using two antiparallel schottky diodes HP2900,
BA481 or similar. Such a mixer has a higher noise figure than
conventional diode mixers, especially when using the suggested
low frequency diodes. On the other hand, the required local
oscillator signal is at 736MHz, only half of the frequency
required for the downconversion (1473MHz).
     The RF module circuit includes a network to supply with
+12V the GaAs FET preamplifier through the RF cable. On the
other hand, the +12V supply voltage for the RF module itself
is taken out of the IF converter, after being filtered by a
choke and a 100uF capacitor.
     The RF module is built in microstrip technology on a
double-sided board made of 0.79mm thick glassfiber-epoxy.
The upper side is shown on Fig. 20 while the lower side is
not etched. The location of the components is shown on Fig. 21.
Before installing the components, L3, L5, L7, L9 and L12
should be grounded by soldering small U-shaped pieces of wire
at the marked locations.
     L1, L4, L6, L8 and L11 are quarter-wavelength chokes.
These are made from about 6cm of 0.15mm thick copper
enamelled wire, tinned for about 5mm at each end. The remaining
wire is wound on a 1mm inner diameter and the finished chokes
are small self-supporting coils. On the other hand, L2 is a
commercial 100uH "molded" choke.
     It is recommended to use thin teflon coax like RG-188 for
the internal RF wiring of the GPS receiver. The braid of the
cable should be soldered directly to the microstrip groundplane
while the central conductor reaches the upper tracks through
a hole in the printed-circuit board. To avoid shorts, the
copper plating around this hole on the groundplane side should
be carefully removed using a much larger (3mm) drill tip.
     The GPS RF module needs some adjustments of the striplines
and these are best performed after all of the receiver hardware
is assembled. L3, L5, L7 and L9 usually need to be trimmed
shorter by about 1mm at the open end to acheive the maximum
gain at 1575MHz. On the other hand, L10 and L12 may need some
small pieces of copper foil (about 7mmx7mm) at different
locations along these stirplines to acheive the best noise
figure from the diodes actually used in the mixer.

4.4. GPS IF converter
---------------------
     The GPS IF strip includes a second downconversion to
10MHz, signal amplification and limiting at 10MHz and the
generation of all required local oscillator and clock signals
from a single master frequency reference.
     The second downconversion to 10MHz and the LO frequency
generation is included in the GPS IF converter module shown on
Fig. 22 and Fig. 23. The GPS IF converter module includes a
6139kHz crystal oscillator (Fig. 23). This frequency is used
both for signal sampling and suitably multiplied for both
downconversions. Since the required short term stability is
very high, in the 1.E-9 range, to be able to demodulate the
50bps PSK navigation data, the crystal oscillator has its own
supply regulator 7805 and is followed by two buffer stages.
     The crystal oscillator output frequency is first
multiplied by five to obtain 30.7MHz and then by three to



l- 30 -
l
obtain the 92MHz required for the second downconversion. Three
additional frequency-doubler stages are required to obtain the
first downconversion signal at 736MHz from the available 92MHz
signal. The design of all multiplier stages is similar and is
using two tuned circuits in each stage except for the first
stage, where three tuned circuits are necessary due to the
higher multiplication factor.
     The 102MHz IF signal is first amplified (BFX89) and then
filtered (L9 and L10). The second mixer is a simple dual-gate
MOSFET mixer (BF981). The selectivity provided by the tuned
circuits at 102MHz (L9 and L10) and at 10MHz (L11) is already
comparable to the GPS C/A-code signal bandwidth (2MHz).
In fact, L11 already requires damping resistors to acheive the
required bandwidth.
     The GPS IF converter is built on a single-sided board as
shown on Fig. 24. The location of the components is shown on
Fig. 25. Due to the limited space all of the resistors are
installed vertically. The capacitors are conventional
ceramic discs (except for 100uF) with a pin spacing of 5mm.
Capacitive trimmers are plastic foil types of 7.5mm diameter:
green 4-20pF and yellow 2-10pF. There is also a wire jumper
marked with "A".
     The BFX89 is used as an universal RF transistor in this
module and has many possible replacements: BFY90, BFW30 etc.
The four leads of the BF981 MOSFET are bent so that the device
is inserted in the printed-circuit board with the marking
towards the board. The 7805 regulator does not require a
heat sink provided that it is a TO-220 version.
     The GPS IF converter includes several inductors. Most of
them are air-wound, self-supporting coils wound with copper
enamelled wire of either 0.5mm or 1mm diameter. The turns of
these coils are not spaced and the leads go straight through
the printed-circuit board without any additional bending or
forming. In these way the coils themselves have about 1/4 of
a turn less than specified in the following paragraph.
     L1 and L2 have 3 turns each of 1mm wire wound on a 4mm
inner diameter. L3 has 5 turns of 0.5mm wire wound on a 3mm
inner diameter. L4 and L5 have two turns each of 1mm wire
wound on a 3mm inner diameter. L6 has 3 turns of 0.5mm wire
wound on 3mm inner diameter. L7 and L8 have one single turn
(or "U" loop) of 1mm wire with a 3mm inner diameter.
L9 and L10 have 5 turns each of 0.5mm wire on a 4mm inner
diameter. Finally, L13 and L14 have 6 turns each of 0.5mm
wire wound on a 4mm inner diameter. L13 has an additional
coupling loop of one single turn around the main winding.
     L11, L15, L16, L17 and L18 are wound on standard cores
for IF transformers (Toko or Mitsumi) with the external
dimensions of 10mmX10mm. L11 should have about 4.5uH and in
practice this means 15 turns of 0.15mm diameter copper
enamelled wire on a 10.7MHz IF transformer core set including
a fixed central ferrite core, an adjustable ferrite cup,
various plastic support parts and a metal shielding can.
L15, L16 and L17 should have about 0.4uH and in practice
have 6 turns of 0.15mm diameter copper enamelled wire on a
36MHz IF transformer core set including a plastic support
with a central adjustable ferrite screw, a plastic cap and
a metal shielding can.
     The exact value of L18 depends on the crystal used and
the frequency required. In all of the prototypes built



l- 31 -
l
inexpensive computer crystals designed for 6144kHz were used.
These require quite a large inductivity to be pulled 5kHz
down to about 6139kHz. An inductivity around 40uH is required
for this shift. The exact value depends much on the crystal
used and the parasitic capacitances of the circuit. Since the
performance of the GPS receiver depends on the stability of
this master crystal oscillator, also L18 needs to be very
stable. Therefore a 36MHz IF transformer core set is
recommended and the latter requires about 60 turns of 0.08mm
diameter copper enamelled wire.
     Finally, L12 is a 100uH "molded" choke.
     The GPS IF converter has several connections. The two coax
cables carrying IF and LO signals to the RF module and the
+12V supply wire for the RF module are all soldered directly
to the bottom side of the IF converter module. The 10MHz IF
output, the 6139kHz clock output and the +12V supply
voltage are available on a 7-pin connector obtained from a
piece of a good-quality IC socket with round contacts.
     The GPS IF module requires several adjustments, but the
crystal oscillator should be adjusted first to roughly 6139kHz.
Then the multiplier chain should be adjusted. Each multiplier
stage should be adjusted to provide the maximum signal at the
required frequency to the next stage. The levels of the RF
signals can be easily monitored with a DC voltmeter, since
they are rectified by the BE junction of the next stage.
Without any RF input, the DC voltage is set to about 0.7V
across the BE junction. When the multiplier chain is opearting
correctly, this voltage should decrease down to about zero
and may even become negative. If the transistor base goes
more negative than -0.5V, RF transistors may be damaged and
this should be avoided by decreasing the values of the coupling
capacitors.
     Of course, the voltmeter required for these adjustments
should only be connected through a RF choke to avoid disturbing
the RF circuit. A 10kohm resistor may also be used as a RF
choke. In this way all of the multiplier stages can be adjusted
except the last one to 736MHz, since no BE junction follows
this stage. The level of the 736MHz signal is monitored in a
different way, by connecting a DC ohmmeter to the IF output of
the mixer. The higher the LO signal level, the lower the
resistance measured by the ohmmeter.
     The signal circuits (L9, L10 and L11) are best adjusted
after the receiver is completely assembled, since the following
IF amplifier has a S-meter output. A grid-dip meter can be
used as a signal source at 102MHz. The trimmers in parallel to
L9 and L10 tune almost to their maximum capacity and L10 may
sometimes require an additional capacitor in parallel.
The final adjustment of the signal circuits is best performed
on a real GPS signal obtained from a directional antenna
(a 15 turn helix or a small dish) pointed to a GPS satellite.
     Finally, the crystal oscillator should be adjusted to the
exact frequency required by the software. For the current
version V122 the exact frequency is 6139.050kHz, but this may
change in the future. The exact frequency is specified in
the program listing.

4.5. GLONASS RF module
----------------------
     The GLONASS receiver requires a tunable downconverter



l- 32 -
l
across all of the 25 GLONASS channels spacing from 1602MHz to
1615.5MHz, therefore its design is more complicated than the
GPS counterpart. The GLONASS downconverter is divided into
four modules for shielding purposes and differences in the
construction technology: a RF module and a PLL synthesizer
converter built in microstrip technology and an IF converter
and synthesizer logic built on simple, single-sided printed
circuit boards.
     The circuit diagram of the GLONASS RF module is shown
on Fig. 26. The GLONASS RF module includes two selective RF
amplifier stages, the first receiver mixer to the first
(fixed) IF of 118.7MHz, and a VCO followed by a buffer stage.
The two RF amplifier stages are identical and use MRF571
transistors. Since the GLONASS RF module is built on a lossy,
but thicker laminate than GPS, the losses in the RF filters
are lower and two amplifier stages provide enough gain.
     The VCO includes an amplifier (BFR91) and a
highly-selective interdigital filter feedback network. Such
a VCO can only cover a very limited frequency range (about 10%
around the central frequency), but its phase noise is very
low. The VCO is tuned by a BB105 varicap in the central finger
of the interdigital feedback network.
     The VCO is followed by a buffer stage with another BFR91.
A microstrip coupler takes part of the VCO output signal to
drive the PLL circuits. The VCO and RF signals are then
combined in an interdigital filter network to feed the
mixer diode HP2900 or BA481.
     The GLONASS RF module circuit includes a network to supply
with +12V the GaAs FET preamplifier through the RF cable.
     The GLONASS RF module is built in microstrip technology on
a double-sided board made of 1.57mm thick glassfiber-epoxy.
The upper side is shown on Fig. 27 while the lower side is
not etched. The location of the components is shown on Fig. 28.
Before installing the components, the resonators of L3, L5, L6
and L7 should be grounded by soldering short pieces of 1mm
diameter copper wire at the marked locations. The transistors
and diodes are installed in 6mm diameter holes in the printed
circuit board.
     L1, L4, L8 and L12 are quarter-wavelength chokes. These
are made from about 6cm of 0.15mm thick copper enamelled wire,
tinned for about 5mm at each end. The remaining wire is wound
on a 1mm inner diameter and the finished chokes are small
self-supporting coils. On the other hand, L2, L9 and L11 are
commercial 120uH "molded" chokes.
     RF interconnections inside the GLONASS receiver are made
with thin teflon coax like RG-188, installed just like in the
GPS receiver front end. On the other hand, GLONASS microstrip
modules include feedthrough capacitors to save space on the
printed-circuit boards. The feedthrough capacitors are
soldered to the microstrip groundplane from the bottom side.
Some components, like chokes and resistors in the supply
network, are also installed on the bottom side of the
microstrip boards.
     The GLONASS RF module only needs few adjustments, mainly
to the VCO feedback network. To cover the desired frequency
range, the central finger usually needs to be trimmed shorter
by several mm. The two side fingers may need adjustments if
the VCO stops oscillating at band edges. The remaining
interdigital filters usually do not need any adjustments to



l- 33 -
l
provide the best performance in the desired frequency range.
If the VCO is operating correctly, the mixer diode will
provide a rectified voltage of about -0.4V across the 150ohm
resistor.

4.6. GLONASS IF converter
-------------------------
     The GLONASS IF strip includes a second downconversion to
10.7MHz, signal amplification and limiting at 10.7MHz and the
generation of the required local oscillator and clock signals
from a single master frequency reference.
     The second downconversion to 10.7MHz and the LO frequency
generation is included in the GLONASS IF converter module shown
on Fig. 29. The GLONASS IF converter module includes a 18MHz
master crystal oscillator. This frequency is used, divided by
four, for signal sampling, divided by 32 as the PLL reference
frequency and suitably multiplied for the second signal
downconversion and for the PLL downconversion.
     The GLONASS IF module only includes the oscillator and
some multiplier stages. The dividers are located in the PLL
synthesizer logic module and the last frequency multiplier is
in the PLL synthesizer converter. Like in the GPS receiver,
the required short term stability is very high, in the 1.E-9
range, to be able to demodulate the 50bps PSK navigation data
Therefore the crystal oscillator has its own supply regulator
7805 and is followed by two buffer stages just like in the
GPS IF converter module.
     The crystal oscillator output frequency is first
multiplied by three to obtain 54MHz. This signal is then
doubled to 108MHz for the second downconversion and multiplied
by three to obtain 162MHz to drive the PLL synthesizer
converter, using two separate multiplier stages fed by the
same 54MHz signal. The 162MHz signal is further amplified in
a buffer stage (BFR96) to drive the SRD multiplier in the
PLL synthesizer converter.
     Since the described GLONASS receiver includes a more
complicated RF front-end than GPS, more filtering is required
in all multiplier stages to avoid spurious frequencies.
Therefore multiplier stages may have three or even more tuned
circuits on their outputs.
     The 118.7MHz IF signal is filtered (L9, L10 and L11) and
amplified (BFX89). The second mixer is a simple dual-gate
MOSFET mixer (BF981). The selectivity provided by the tuned
circuits at 118.7MHz (L9, L10 and L11) and at 10.7MHz (L12) is
already comparable to the GLONASS C/A-code signal bandwidth
(1.2MHz). In fact, L12 already requires damping resistors to
acheive the required bandwidth.
     The GLONASS IF converter is built on a single-sided board
as shown on Fig. 30. The location of the components is shown on
Fig. 31. Due to the limited space all of the resistors are
installed vertically. The capacitors are conventional
ceramic discs (except for 100uF) with a pin spacing of 5mm.
Capacitive trimmers 4-20pF are a plastic foil type of 7.5mm
diameter, marked with a green body. There is also a wire jumper
marked with "A".
     The BFX89 is used as an universal RF transistor like in
the GPS IF converter. Also the BF981 is installed just like
in the GPS IF converter module and a TO-220 case 7805 regulator
is recommended so that no heat sink is required.



l- 34 -
l
     The GLONASS IF converter includes several inductors. Most
of them are air-wound, self-supporting coils wound with copper
enamelled wire of 0.5mm diameter. The turns of these coils are
not spaced and the leads go straight through the
printed-circuit board without any additional bending or
forming. In these way the coils themselves have about 1/4 of
a turn less than specified in the following paragraph.
     L5, L6 and L7 have 4 turns each wound on a 3mm inner
diameter. L9, L10 and L11 have 4 turns wound on a 4mm inner
diameter. L13 and L14 have 5 turns wound on a 4mm inner
diameter. L14 has an additional coupling loop of one single
turn around the main winding.
     L1, L2, L3, L4 and L12 are wound on standard cores
for IF transformers (Toko or Mitsumi) with the external
dimensions of 10mmX10mm. L12 should have about 4.5uH and in
practice this means 15 turns of 0.15mm diameter copper
enamelled wire on a 10.7MHz IF transformer core set including
a fixed central ferrite core, an adjustable ferrite cup,
various plastic support parts and a metal shielding can.
L2, L3 and L4 should have about 0.13uH and in practice
have 3 turns of 0.3mm diameter copper enamelled wire on a
36MHz IF transformer core set including a plastic support
with a central adjustable ferrite screw, a plastic cap and
a metal shielding can.
     The exact value of L1 depends on the crystal used and
the frequency required. In all of the prototypes built
inexpensive computer crystals designed for 18000kHz, series
resonance, were used. These require a small inductivity
in series to compensate for the feedback capacitors of the
oscillator network. In practice about 2uH were required,
corresponding to 16 turns of 0.15mm diameter copper enamelled
wire on a 36MHz IF transformer core set.
     Finally, L8 is a VK200 "six-hole" ferrite choke and L15
is a 100uH "molded" choke.
     The GLONASS IF converter module has several connections.
The two cables carrying the 118.7MHz IF from the RF module and
the 162MHz LO to the PLL synthesizer converter are all soldered
directly to the bottom side of the IF converter module.
The 10.7MHz IF output, the 18MHz clock output and the +12V
supply voltage are available on a 7-pin connector obtained from
a piece of a good-quality IC socket with round contacts.
     In the GLONASS IF converter module the multiplier stages
should be aligned first, just like in the similar GPS module.
However, only the output of the first multiplier stage to 54MHz
can be moinitored as a dip of the following stage base voltage.
The output of the 108MHz multiplier may be observed as a dip
in the drain voltage of the BF981 mixer, while the output of
the 162MHz multiplier may be measured as the rectified voltage
by the SRD multiplier in the PLL synthesizer converter.
     The signal circuits (L9, L10, L11 and L12) are best
adjusted after the receiver is completely assembled, since the
following IF amplifier has a S-meter output. A grid-dip meter
can used as a signal source at 118.7MHz. The trimmers in
parallel to L9, L10 and L11 tune almost to their maximum
capacity. The final adjustment of the signal circuits is best
performed on a real GLONASS signal obtained from a directional
antenna (a 15 turn helix or a small dish) pointed to a GLONASS
satellite.
     Finally, the crystal oscillator should be adjusted to the



l- 35 -
l
exact frequency required by the software. For the current
version V39 the exact frequency is 18000.000kHz, but this may
change in the future. The exact frequency is specified in
the program listing.

4.7. GLONASS PLL synthesizer converter
--------------------------------------
     A single-channel GLONASS receiver requires a fast-settling
frequency synthesizer, since the receiver is continuously
switching among different frequency channels. Besides this
requirement the synthesizer should have a low phase noise.
To limit group-delay variations the synthesizer should supply
a variable frequency already to the first downconverter.
     All these requirements ask for a PLL synthesizer with
a frequency downconverter in the feedback loop, to decrease
the divider modulo and increase the loop gain. Therefore, the
GLONASS PLL synthesizer includes a VCO in the RF module,
a downconverter and conventional PLL synthesizer logic like
variable modulo dividers and a frequency/phase comparator.
     The circuit diagram of the GLONASS PLL synthesizer
converter is shown on Fig. 32. The circuit includes another
buffer stage for the VCO signal around 1490MHz, a step-recovery
diode (SRD) frequency multiplier by 9, to get 1458MHz from
the available 162MHz, a mixer diode and an IF amplifier stage.
The VCO buffer stage (BFR90) is required to avoid getting any
unwanted spurious signals back in the GLONASS RF module.
     The SRD multiplier uses a very inefficient silicon
PN-junction diode 1N4148. Other diodes like VHF TV tuner
bandswitching diodes (BA182 or BA482) provide an up to 20dB
stronger signal at 1458MHz in the same circuit, but a higher
signal level is not required here and it is even harmful,
since it may get in the RF module and cause unwanted mixing
products. In practice it is thus convenient to keep the
1458MHz signal level low and drive the mixer diode into
the nonlinear region with the 1490MHz VCO signal.
     To avoid any spurious generation all signal levels are
kept low. Even the buffered VCO signal amounts to only a few
hundred mV on the mixer diode HP2900 (or BA481) while the
1458MHz signal level is much lower. To operate efficiently at
low signal levels the mixer diode receives a DC bias current.
     The PLL IF signal then needs much amplification to reach
the TTL level required by the variable-modulo counter. The
first PLL IF amplifier stage (BFR90) is built in the PLL
converter module. The following PLL IF amplifier stages are
located in the PLL synthesizer logic module for shielding
purposes, since harmonics of the PLL IF fall in the first IF
(118.7MHz) frequency range of the described GLONASS receiver.
     The GLONASS PLL synthesizer converter is built in
microstrip technology on a double-sided board made of 1.57mm
thick glassfiber-epoxy. The upper side is shown on Fig. 33
while the lower side is not etched. The location of the
components is shown on Fig. 34. Before installing the
components, the resonators of L1, L3 and L4 should be grounded
by soldering short pieces of 1mm diameter copper wire at the
marked locations. The transistors and diodes are installed in
6mm diameter holes in the printed circuit board.
     L2, L5, L7 and L8 are quarter-wavelength chokes. These
are made from about 6cm of 0.15mm thick copper enamelled wire,
tinned for about 5mm at each end. The remaining wire is wound



l- 36 -
l
on a 1mm inner diameter and the finished chokes are small
self-supporting coils. L6 is a self-supporting coil with 3
turns of 0.5mm diameter copper enamelled wire wound on a
3mm inner diameter.
     The microstrip filters in the GLONASS PLL synthesizer
converter usually do not require any trimming. The 10kohm
trimmer for the SRD bias current is usually set to 5kohm.
The SRD multiplier will operate correctly if the rectified
DC voltage by the 1N4148 diode amounts to about 2V.

4.8. GLONASS PLL synthesizer logic
----------------------------------
     To convert the frequency range form 1602MHz to 1615.5MHz
down to 118.6875MHz, the VCO must operate in the frequency
range from 1483.3125MHz to 1496.8125MHz. Subtracting 1458MHz
in the PLL synthesizer converter, this frequency range is
downconverted to 25.3125MHz to 38.8125MHz. The latter frequency
range corresponds to integer multiples ranging between 45 and
69 of the GLONASS channel spacing of 562.5kHz.
     The design of the PLL synthesizer logic is therefore
straightforward and the corresponding circuit diagram is shown
on Fig. 35. The PLL synthesizer logic includes a PLL IF
amplifier, a variable modulo divider for the PLL IF, a fixed
divider by 32 to obtain the 562.5kHz reference and a
frequency/phase comparator.
     The PLL IF signal in the range from 25MHz to 39MHz is
first amplified to a TTL level in a two stage amplifier.
The gain of this amplifier is set higher than required to
have a considerable safety margin. The base bias resistor
of the second stage may need some trimming although the
suggested value of 2.2kohm will usually work.
     The programmable modulo counter is built from two
synchronous counters: a 74F161 and a 74HC161. A 74Fxxx counter
is required in the first stage to operate reliably at the
highest frequency, since the PLL IF may be several tens of MHz
above 39MHz in the unlocked state!
     The counter feedback network includes an inverter and a
74HC157 multiplexer. The modulo of the second counter (74HC161)
is programmed directly. The modulo of the first counter
(74F161) is set to 10 except during the last state of the
second counter, when the 74HC157 switches the 74F161 preset
inputs to the 4094 outputs. In this way setting the modulo of
the second counter changes the whole divider modulo in steps
of 10, while setting the modulo of the first counter during
the last cycle only provides the single-count steps.
     The 4094 is a 8-bit shift register with output latches.
It is used as a serial-to-parallel interface driven by the
computer. Of the eight available output lines, four are used
to control the modulo of the 74HC161 counter and the other
four to control the modulo of the 74F161 during the last cycle
of the 74HC161. One should be especially careful when
programming the modulo of the divider: the data is inverted
and the first divider modulo should never be set too low to
allow for the delays in the slower 74HCxxx logic!
     The 18MHz master reference frequency is also amplified to
TTL level in a single-stage amplifier (2N2369). A 74HC393
counter divides this frequency by four to obtain the 4500kHz
sampling frequency and by 32 to obtain the PLL reference
frequency. The 4500kHz signal is attenuated with a resistor



l- 37 -
l
network to limit spurious radiations. It is then amplified
back to TTL level in the dedicated DSP hardware module.
     The frequency/phase comparator is a charge-pump circuit
including two D-flip-flops (74HC74), a feedback network with
a NAND gate and charge-pump switches with schottky diodes.
The backlash problem is solved by making the charge-pump
circuit faster than the feedback network. This does not
make the phase detector linear yet, but provides a stable
locking point for the PLL with no dead zone and produces a
very clean synthesizer signal spectrum. An additional NAND
gate provides a LOCK signal for test purposes.
     The GLONASS PLL synthesizer logic is built on a
single-sided printed circuit board as shown on Fig. 36. The
location of the components is shown on Fig. 37. There are
three wire jumpers on this board and two of them are installed
below the 74HC157 multiplexer. A complex single-sided board
also places some constraints on the installation of the
resistors: those with a 10mm hole spacing are installed
horizontally while the others are installed vertically to
save space. All of the capacitors are ceramic with a 5mm
pin spacing, including the 1uF (multilayer).
     L1 is a commercial 100uH "molded" choke. The module has
three connectors with 3, 4 and 7 contacts, made from pieces
of good-quality IC sockets. The integrated circuits should
be soldered directly on the board except for the 4094. It
is recommended to install this IC on a socket so that
it can be removed from the circuit and replaced by wire
jumpers to be able to test the synthesizer without the
computer running.
     The GLONASS synthesizer logic may require a single
adjustment: the bias resistor for the second PLL IF
amplifier stage. This may be adjusted if the output
DC voltage deviates much from 1.3V (with no input signal) or
if the programmable counter does not operate reliably.

4.9. GPS/GLONASS second IF amplifier
------------------------------------
     Both GPS and GLONASS receivers require a limiting IF
amplifier at the final IF frequency around 10MHz. The circuit
diagram of this amplifier is shown on Fig. 38. The GPS/GLONASS
second IF amplifier includes a first stage with a bipolar
transistor BFX89 and a second stage with the integrated
circuit CA3089.
     The gain of the first stage is limited by the 22ohm
resistor in the emitter circuit. The first stage is followed
by a tuned circuit (L1) to limit broadband noise and avoid
amplifying various spurious signals from the many oscillators
inside a GPS or GLONASS receiver. The damping resistor in
parallel with L1 sets the bandwidth of this tuned circuit
to be comparable to the GPS or GLONASS signal bandwidth.
     The second stage uses a popular FM IF strip integrated
circuit. The latter provides wideband amplification and
limiting, while the discriminator section of this integrated
circuit is not used here. The limited IF output is available
on pin 8 and the signal level amounts to a few hundred
millivolts at 10MHz. This is not enough to drive the following
TTL logic directly and the remaining gain is built inside the
dedicated DSP hardware module.
     The CA3089 integrated circuit includes a S-meter output.



l- 38 -
l
The latter is of little use during actual receiver operation,
since the satellite signal levels are comparable to noise in
the wideband IF. In the case of a GPS receiver, the S-meter
output can only show the sum of all of the signals present.
On the other hand, the S-meter output is very useful during
receiver testing and alignment of the RF, first and second IF
tuned circuits.
     Both GPS and GLONASS receivers include a S-meter function
inside the narrowband IF processing. Since the latter is done
in software, the real receiver S-meter as displayed on the LCD
is just another software function and is NOT related to the
hardware S-meter output of the IF strip.
     The GPS/GLONASS second IF amplifier is built on a
single-sided printed circuit board as shown on Fig. 39. The
location of the components is shown on Fig. 40. Due to the
limited space all of the resistors are installed vertically.
The capacitors are conventional ceramic discs (except for
22uF) with a pin spacing of 5mm.
     L1 is wound on a 10.7MHz IF transformer core set
incliding a fixed central ferrite core, an adjustable ferrite
cup, various plastic support parts and a metal shielding can.
The primary (resonant) winding of L1 has 10 turns of 0.15mm
diameter copper enamelled wire, corresponding to an
inductivity of about 2uH. The secondary (link) winding has
two turns of the same wire. L2 is a 100uH "molded" choke.
     The second IF amplifier module has two coonectors: a
2-pin connector for the input and a 5-pin connector for the
output and supply voltage, obtained from pieces of
a good-quality IC socket with round contacts.
     The tuned circuit with L1 is best adjusted after the GPS
or GLONASS receiver is completely assembled, finding the
maximun DC voltage on the "test" S-meter output in the same
IF module. The final adjustment of all signal circuits is
best performed on a real satellite signal obtained from a
directional antenna (a 15 turn helix or a small dish) pointed
to an operating navigation satellite. A directional antenna
should provide a higher-than-usual signal-to-noise ratio of
more than 10dB already in the wideband IF. A high SNR is
required to tune the circuits to the signal peak and not to
noise or some spuriuous signals while observing the voltage
on the "test" S-meter output.

4.10. GPS/GLONASS DSP hardware
------------------------------
     The theory of operation of the dedicated GPS/GLONASS DSP
hardware has already been discussed in 3.6. Therefore the
practical implementation will only be described in the
following paragraph.
     The dedicated GPS/GLONASS DSP hardware is built as a
peripheral plug-in module for the DSP computer [1], [2].
The circuit diagram of the GPS/GLONASS DSP hardware is
shown on Fig. 41 and Fig. 42. The DSP hardware module
includes two amplifiers for the limited IF signal and master
clock coming from the analog part of the GPS or GLONASS
receiver, a look-up table RAM, four signal-despreading
mixers, four correlator counters, all of the timing logic to
scan the look-up table and generate interrupts to the CPU
and all of the interface circuits necessary for the DSP
computer bus.



l- 39 -
l
     The input signal amplifiers are built with 74HC04
inverterts to amplify the input signals of a few hundred
millivolts up to TTL levels. In this way the signal levels
in the analog part of the GPS or GLONASS receiver can be kept
more than 20dB lower, reducing the shielding requirements.
The supply voltage of the 74HC04 is additionally filtered
to reject the disturbs usually present on the +5V computer
bus power supply. The limited input signal is then sampled by
a D-flip-flop (1/2 74HC74). Considering the relationship
between the IF and the sampling frequency, the sampling
operation also provides a third downconversion.
     The look-up tables are stored in a 32kX8 static RAM.
The RAM area is divided into 8 separate areas of 4kbytes
each, selectable through a microprocessor output port. In this
way the look-up table needs not to be rewritten when switching
to another satellite. The receiver is usually time-multiplexed
among four different satellites and all four different look-up
tables are stored in the RAM. When switching to another
satellite, the hardware is simply switched to another look-up
table and this only requires executing a few instructions
instead of rewriting the whole 4kbyte table.
     The 4kbytes of each look-up table are written as bytes by
the microprocessor. The microprocessor writes all of the bytes
to the same location, since the address counter is incremented
automatically after each write operation. In read mode the
look-up table is scanned by the same hardware counter
(74HC4040) clocked at half the sampling frequency (3069.5kHz
for GPS or 2250kHz for GLONASS). The byte data is latched
(74HC273) and then multiplexed to 4 bits (74HC157) to get all
of the four required local signal replicas to be multiplied
(EXOR 74HC86) with each input signal sample. Each look-up
table may be thus up to 8192 samples long. The unused samples
need not be written since they are not used by the hardware.
     The dedicated DSP hardware requires six programmable
counters: four correlation accumulators, a sampling frequency
divider and a variable delay counter, all contained in two
uPD71054 (82C54) integrated circuits. Each uPD71054 contains
three almost independent 16-bit counters that can be
programmed in different ways. For example, the four
correlation counters are clocked with the same signal sampling
frequency and the signals are fed to the GATE inputs, which
are programmed as clock enables.
     The signal sampling frequency (6139 or 4500kHz) is
divided down to 1kHz to match the C/A-code period (1ms). This
signal is also used to request interrupts from the CPU, since
the correlation counters need to be read each millisecond.
After receiving an interrupt request, the CPU will latch
the content of all counters in a single bus operation and then
read the latched content of every single counter in separate
bus operations. The sampling clock divider is also latched and
read and its content is used as an accurate timing reference.
     Every interrupt request sets a flip-flop that needs to be
reset by the microprocessor after the interrupt has been
serviced. Interrupt arm (enable) and reset (disable) is
performed through one (Q4) of the eight output-port bits
provided by the 74HC259 addressable latch. Of the remaining
7 bits, three (Q1, Q2 and Q3) are used to select one of the
eight look-up tables in the RAM and another bit (Q0) is used
to select either write or read mode for the look-up table



l- 40 -
l
logic. The last three bits (Q5, Q6 and Q7) are used to
control the GLONASS PLL modulo or as spares in a GPS receiver.
     The bus interface to the DSP computer bus includes a
bidirectional data-bus buffer (74HC245) and an address
selection logic (two 74HC138s and 74HC10). The bus interface
does not request any wait states from the MC68010 CPU. The
address decoding for the uPD71054 programmable counters must
allow simultaneous write operations to both control registers
of both peripherals, to be able to latch the content of all
of the counters exactly at the same time. Finally, the RESET
signal is fed to the 74HC259 adressable latch essentially
to prevent any interrupts or other unintended operations
before the whole DSP hardware is correctly initialized.
     The bus addresses are assigned as follows:

$E0001   - Disable look-up table write mode
$E0003   - Enable look-up table write mode

$E0009   - Look-up table address A2 reset
$E000B   - Look-up table address A2 set
$E0041   - Look-up table address A1 reset
$E0043   - Look-up table address A1 set
$E0049   - Look-up table address A0 reset
$E004B   - Look-up table address A0 set

$E0081   - Reset & disable 1ms interrupt
$E0083   - Enable 1ms interrupt
$E0082   - Reset & enable 1ms interrupt, long transfer!

$E0089   - GLONASS PLL modulo STROBE reset
$E008B   - GLONASS PLL modulo STROBE set
$E00C1   - GLONASS PLL modulo DATA reset
$E00C3   - GLONASS PLL modulo DATA set
$E00C9   - GLONASS PLL modulo CLOCK reset
$E00CB   - GLONASS PLL modulo CLOCK set

$E800B   - Common WRITE to both 71054 command registers

$E8041   - 71054 #1 CTR0 - data 0,4 accumulator
$E8043   - 71054 #1 CTR1 - data 1,5 accumulator
$E8049   - 71054 #1 CTR2 - data 3,7 accumulator
$E804B   - 71054 #1 command register

$E8081   - 71054 #2 CTR0 - variable C/A-code delay
$E8083   - 71054 #2 CTR1 - GPS /6139 or GLONASS /4500 clk
$E8089   - 71054 #2 CTR2 - data 2,6 accumulator
$E808B   - 71054 #2 command register

$F8001   - WRITE byte to look-up table

However, one should notice that the remaining addresses in
the range from $E0000 to $FFFFF are not fully or correctly
decoded, although the module will acknowledge the access to
the MC68010. Accessing other addresses in this range (either
reading from or writing to) will probably cause an erratic
operation of the module. The 74HC259 addressable latch is
programmed by writing to the specified locations. Since only
the address is important and the data is ignored, CLR.B
instructions are used to write to single bytes and a CLR.L



l- 41 -
l
instruction is used to reset and arm the interrupt flip-flop.
     The dedicated DSP hardware module is built on a
double-sided printed-circuit board as shown on Fig. 43 and
Fig. 44. The location of the components is shown on Fig. 45.
The single resistors, diodes and the 100uH choke are installed
horizontally. The eight 10kohm resistors are in a single 9-pin
SIL package. The capacitors are ceramic except the 10uF
"tantalum drop" and all have a pin spacing of 5mm.
     The 74HC4040 should NOT be replaced by a standard 4040
device, since the latter is too slow for a correct operation
in the described circuit. To allow an eventual troubleshooting
it is recommended to install at least the two 71054 counters
and the 43256 RAM on good-quality sockets. The speed of the
RAM is unimportant, since even the slowest 150ns static RAMs
are fast enough for this project.
     The dedicated DSP hardware module is inserted in the DSP
computer bus with a 64-pole "eurocard a+c" connector. The
remaining connectors include a 5-pin socket for the input IF
signal and clock, a 4-pin socket for the GLONASS PLL modulo
control and a 8-pin socket for the interrupt selection. All
of these are made from parts of good-quality IC sockets.
     The dedicated DSP hardware module only includes logic
circuits that require no alignments.

4.11. GPS/GLONASS portable receiver CPU
---------------------------------------
     The described GPS or GLONASS receiver can be built as an
interface for the DSP computer [1] and [2] or as a
stand-alone, portable receiver. In the latter case the
receiver needs its own microcomputer with a keyboard and a
LCD display. After considering several possible alternatives,
the simpliest solution resulted in using a suitably modified
CPU board as described in [1] and [2] as the microcomputer.
     The circuit diagram of the modified CPU board is shown
on Fig. 46 and Fig. 47. Since a GPS or GLONASS receiver is a
portable device, the power consumption is important and 74HCxx
logic devices should be used everywhere. This allows to omit
three 3.3kohm pull-up resistors. The original DSP computer CPU
board requires the following modifications:
(1) The pads below the EPROM socket should be connected so
    that pin 27 receives the A14 signal required by the
    27C256 EPROM. Originally this pin is connected to +5V,
    using a 27128 EPROM.
(2) The RAM should be increased from 64kbytes up to 128kbytes.
    This is acheived by piggy-back soldering two additional
    43256 RAM chips on top of the exsisting two RAM chips on
    CPU board. All pins of the additional RAMs are connected
    in parallel with the exsisting RAM pins except for pin 20
    (chip select). The two chip-select pins of the added RAM
    chips are then wired to pin 11 (Q4) of the middle 74HC138
    address decoder.
(3) A HSCH1001 schottky diode should be connected between
    pin 11 (Q4) of the top 74HC138 address decoder and the
    DTACK signal (pin 12 of the 74HC05), to acknowledge the
    additional RAM chips to the CPU.
The keyboard connection remains unchanged. The total/partial
reset switch has a new function with the GPS or GLONASS
software. In the case of a stand-alone, portable receiver,
this input should always be left open (+5V)!



l- 42 -
l
     The parallel output port (uPD71055 channel B) is now used
to command the HD44780 LCD controller. Since there are only
8 output bits available, the HD44780 is driven in the 4-bit
mode, write only. The real-time clock chip uPD4990 is required
by the GPS or GLONASS software and must remain in place.
The INT7 jumper must remain in place for keyboard interrupt
requests while the INT1 jumper is no longer needed, although
it may remain in place.
     The printed circuit board is not modified, as shown on
Fig. 48 and Fig. 49. The additions and modifications are well
visible on the component location plan on Fig. 50. The
connections of the 8-key keyboard and of the LCD controller
are also shown on Fig. 50.
     It is recommended that the CPU board is tested first,
if possible, in a DSP computer and the described modifications
are only applied to a 100% tested and working CPU board.
In particular, the CPU board should be tested at higher clock
frequencies to find any defective components. A 10MHz version
of the MC68010 will usually work up to 15MHz clock frequency
at room temperature, so a 12MHz clock crystal is a safe
choice. The GPS or GLONASS software does not require such a
high clock frequency, but the accuracy of some measurements
is higher and the updating of the display is faster at higher
clock rates.

4.12. 8-key keyboard
--------------------
     A portable GPS/GLONASS receiver requires a small keyboard
to issue commands to the computer. Since a full ASCII keyboard
is unpractical for a portable piece of equipment, a small
8-key keyboard was developed for portable receivers.
     The circuit diagram of the 8-key keyboard is shown on
Fig. 51. The 8 keys close towards ground, otherwise the input
lines are held high by pull-up resistors. A priority encoder
(74HC148) is used to encode the 8 keys into 3 bits. A double
monostable (74HC4538) is used to generate the strobe pulse
after a key is depressed.
     The 8-key keyboard is assembled on a small single-sided
printed circuit board shown on Fig. 52. This printed circuit
board was designed to fit on the front panel of the receiver
and carry eight square (12.7mmX12.7mm) pushbuttons. The
location of the components is shown on Fig. 53. Due to the
space constraints all of the components should have a low
profile and small dimensions. The capacitors have a 2.5mm
pin spacing and the resistors are installed horizontally.
The eight 10kohm resistor network in a SIL package should
be first soldered in place and then bent towards the circuit
board. The 6-pin connector is installed on the back - solder
side of the board!
     The GPS/GLONASS receiver software only accepts ASCII
characters from $30 to $37 as commands, corresponding to
numerals 0 to 7. These can be generated by a standard ASCII
keyboard with a parallel output or by suitably wiring the
described 8-key keyboard. In particular, to obtain the
codes between $30 and $37, the outputs D0, D1 and D2 should
be wired to the corresponding inputs on the CPU board.
In addition, D3, D6 and D7 should be connected to ground and
D4 and D5 to +5V. All these connections, including the supply
rails and the strobe signal, were already shown on Fig. 50.



l- 43 -
l
4.13 LCD display module
-----------------------
     The only practical display for a portable GPS/GLONASS
receiver is a LCD module with built-in drivers. Such modules
are available in many different sizes and shapes and may
or may not be equipped with a display controller. LCD modules
with a built-in controller are easy to use, since the
interfacing to any microprocessor is very simple: it is
identical to a parallel I/O port.
     Most small dot-matrix alphanumeric LCD modules use the
Hitachi HD44780 LCD controller. This integrated circuit has a
built-in, extended ASCII character generator, a display
area RAM including up to two rows of 40 characters each and
all of the timing circuits to drive the LCD. Modules using the
HD44780 controller may have a different number of characters
per row or rows displayed, the total number of characters is
however limited by the internal RAM to 80. Since the HD44780
SMD flat package has only 80 pins, additional LCD driver chips
(HD44100) are used in most LCD modules.
     A LCD module with two lines of 40 ASCII characters each
was selected for the described GPS/GLONASS receiver. Such
a LCD module includes the liquid-crystal display itself,
one HD44780 LCD controller and four HD44100 LCD drivers.
Further, the display module may include some form of
illuminating the LCD, either EL foil or LED. The latter
is recommended if the GPS/GLONASS receiver is to be used at
night as well.
     Although such display modules are available from several
different manufacturers, they all have the same dimensions
of the carrier printed circuit board: 182mm(width)X
X33.5mm(height)X13mm(thickness) and the same 14-pin electrical
connector. The pin numbers are usually marked on the
printed-circuit board and the pin allocations are as follows:

pin  1    Vss    Ground
pin  2    Vdd    +5V supply
pin  3    Vo     LCD voltage, tap of the contrast control pot
pin  4    RS     Register Select, 0=instruction, 1=data
pin  5    R/W    Read/Write, 0=write, 1=read
pin  6    E      Enable, 0=inactive, 1=active
pin  7    DB0    LSB data, 8-bit bus
pin  8    DB1
pin  9    DB2
pin 10    DB3
pin 11    DB4    LSB data, 4-bit bus
pin 12    DB5
pin 13    DB6
pin 14    DB7    MSB data

EL or LED backlight may have two attitional pins on the
connector or solder pads on the printed-circuit board.
     When LCDs are driven in time multiplex, the adjustment
of the voltage applied to the LCD is critical to obtain
a good contrast. A contrast control potentiometer is
usually provided to adjust the best available contrast for
a given viewing angle of the LCD. This potentiometer provides
the Vo voltage to the LCD module. Modern LCD modules require
operating voltages of less than 5V, so the resistor terminals
can be conveniently connected to ground and to +5V while the



l- 44 -
l
tap is connected to the Vo input.
     Due to the internal circuits of the LCD controller and
driver chips, the internal LCD ground is Vdd (+5V). The
voltage across the LCD equals the potential difference
between Vdd and Vo. The current through the Vo terminal is
very small, so a 10kohm potentiometer with a linear taper
is sufficient for the LCD contrast control.
     If using a LCD module with an EL foil backlight, a
suitable power supply needs to be built. The EL foil usually
requires a supply voltage of about 110V at about 500Hz.
The EL foil behaves electrically as a lossy capacitor. The
voltage across its terminals affects the amount of light
produced while the frequency affects the colour of the light.
     A suitable power supply is shown on Fig. 54 and includes
a power oscillator (555), a step-up transformer and a few EMI
filtering components. For 500Hz operation a conventional
mains transformer with a laminated core can be used, either
220V/9V or 220V/6V, of course with the primary and secondary
windings interchanged. A 1.2W or 1.5W transformer is usually
the smallest available, although it is still quite large
for this application.
     The printed-circuit board for the EL foil supply is
shown on Fig. 55 and the related location of components on
Fig. 56. The power drain of the whole circuit is about 50mA
from a 12VDC power supply, when the output is connected to the
load. Since the oscillator feedback is taken from the output
(pin 3 of the 555), some 555 ICs may not operate in a stable
way in this circuit. In the latter case the solution is to
increase the oscillator frequency by decreasing the 100nF
capacitor.
     Of course, a LED backlight is much easier to use and
usually only requires a 5VDC supply.

4.14. Power supply & RESET circuit
----------------------------------
     The described GPS/GLONASS receiver is intended to be
operated from a 12V battery, with the negative grounded. This
supply voltage is common to all portable and mobile equipment.
The analog circuits of the GPS/GLONASS receiver are already
designed to operate from a +12V supply rail, since this
voltage represents a convenient choice.
     Of course, digital circuits require a +5V supply voltage.
But besides the +5V supply there are other requirements.
A GPS or GLONASS receiver should include a real-time clock
that operates even when the receiver is powered down.
Similarly, the almanac data including information about the
available satellite orbits should be stored in the computer
memory when the receiver is powered down. Finally, since
the +5V power drain amounts to about one half of the total
power drain of a GPS or GLONASS receiver, the +5V supply
regulator should also have a good efficiency, especially
in a portable receiver.
     The requirements for the microcomputer power supply are
therefore the same as for the DSP computer published in [1]
and [2]. The original DSP computer power supply is however
about 10 times too large for this application, so a
scaled-down version is shown on Fig. 57. The latter includes a
switching regulator from 12V to 5V, a memory (clock) backup
battery and a very reliable RESET circuit.



l- 45 -
l
     The microcomputer power supply is built on a single-sided
printed circuit as shown on Fig. 58. The corresponding
location of components is shown on Fig. 59. All of the
resistors, diodes and chokes are installed horizontally.
All of the capacitors have a 5mm pin spacing. Several mounting
holes and related pads are provided for different style NiCd
batteries.
     The power supply is designed for a 400mA to 500mA load
on the +5V output. For this load the BD138 power switch does
not require a heatsink yet and easily available "molded"
chokes can be used in the switching regulator. In particular,
a 100uH choke with the external dimensions of a 1/2W resistor
will withstand a current of up to 200mA to 300mA, so two such
chokes are used in parallel in the switching regulator.
     The total power drain when using the described power
supply and inculding the analog section, amounts to about 4W
for a portable GPS receiver and to about 6W for a portable
GLONASS receiver, both with the LCD backlight off.

4.15. GPS/GLONASS receiver module location
------------------------------------------
     A GPS or GLONASS receiver includes both low-level RF
signal amplification and processing and very noisy digital
circuits, so the module location has to be selected carefully
and some shielding is required in any case.
     In the case of a GPS or GLONASS receiver operating as
a peripheral for the DSP computer, the RF part of the
receiver should be built in its own enclosure while the
dedicated DSP hardware module is plugged in the computer bus.
Of course it is assumed that the computer already has its own
shielded enclosure.
     The GPS-receiver RF part needs no additional internal
shields among the three modules: RF, IF converter and IF
amplifier. The GLONASS-receiver RF part is more complicated
and requires some shielding. In particular, the GLONASS PLL
synthesizer logic needs to be well shielded from the remaining
modules: RF, IF converter, IF amplifier and PLL converter.
     In the case of a stand-alone, portable GPS or GLONASS
receiver it is of course desirable to have the complete
receiver packaged in one single enclosure. It is suggested
that enclosure is made of unpainted aluminum sheet to have a
good electrical contact among the various parts. Such a
container is made of a rectangular frame and two covers
installed with self-locking screws. The frame has an
additional internal plate that divides the internal volume
in two sections shielded both from the outside and between
themselves. One of the sections is used for the noisy digital
circuits and the other for the low-level RF stages.
"Interference-neutral" modules, like the keyboard or the power
supplies may be installed in either section.
     The suggested module location for a portable GPS receiver
is shown on Fig. 60. The suggested dimensions are
200mm(width)X160mm(depth)X80mm(height). The internal plate
is installed at a height of 30mm, so that the digital section
gets a volume of 200mmX160mmX50mm (top) and the analog section
gets a volume of 200mmX160mmX30mm (bottom). The internal plate
is screwed on the frame on all four sides with many screws
to ensure a good electrical shielding.
     The two modules with 64-pole "eurocard" connectors are



l- 46 -
l
installed on a short bus "motherboard" with just two female
connectors with the corresponding pins tied together. The bus
can be made by cutting a piece of the DSP computer bus board
or by simply installing the two connectors on a piece of an
universal board with holes in a uniform 0.1" raster.
     The connections between the analog and digital parts
do not require feedthrough capacitors if they are routed
carefully, away from sensitive or very noisy components.
Sometimes it results useful to additionally ground the shields
of coaxial cables when crossing the internal plate.
     The suggested module location for a portable GLONASS
receiver is shown on Fig. 61. The suggested dimensions are
240mm(width)X160mm(depth)X80mm(height). The internal plate
is installed at a height of 30mm, so that the digital section
gets a volume of 240mmX160mmX50mm (top) and the analog section
gets a volume of 240mmX160mmX30mm (bottom). Like in the GPS RX
the internal plate is screwed on the frame on all four sides.
In addition there is a small shield between the RF module
and the remaining modules in the analog part. On the other
hand, in the GLONASS receiver the computer power supply is
installed in the digital section, together with the PLL
synthesizer logic.








































l- 47 -
l
5. GPS & GLONASS receiver software
==================================

5.1. GPS/GLONASS receiver software overview
-------------------------------------------
     Satellite navigation is one of the first applications
that totally depends on the availability of suitable computers
and the corresponding software. Although initially the digital
computer was only intended to solve the navigation equations,
other tasks were being gradually added to simplify
the hardware in front of and behind the computer itself.
In the described GPS/GLONASS receiver even most of the signal
processing is performed in software, just to keep the analog
front-end and dedicated DSP hardware as simple as possible.
     The software running in a GPS or GLONASS receiver is
therefore very complex and includes a variety of very
different functions. For example, digital signal processing
requires quick but simple integer arithmetics while solving
the navigation equations requires high-accuracy floating-point
arithmetics. The latter does not need to be as quick as the
former signal processing, but a considerable number of
operations still need to be performed in a limited amount of
time.
     To make a fair comparison one should consider the
developement time for the hardware and for the software.
In the case of the described navigation receiver, the
developement of the software required between two and three
times the amount of time required to develop the hardware!
     Unfortunately it is much more difficult to describe down
to the smallest detail the software than the hardware. For the
hardware one can draw the circuit diagrams and prepare
detailed parts lists. On the other hand, detailed descriptions
of the software tend to become boring and minor details tend
to hide the real problem being solved.
     Therefore only the major functions performed by the
software will be described in this article. These include
signal acquisition and processing, almanac and precision
ephemeris data collection, time and frequency measurements,
solving the navigation equations and data display in a
suitable format for the user. At the end the user interface:
display menus and user commands, will be described in detail.
     The overall software is written in different languages
due to the differing functions to be performed: MC68010
assembly language, DSP computer high-level language and even
directly in machine code.
     The digital signal processing software is written in
the MC68010 assembly language. The corresponding file has
the extension .ASM. This file is first compiled into machine
code and then into hexadecimal format, so that it can be
easily inserted in the DSP computer high-level language.
     The orbital mechanics and navigation equation part is
written in the DSP comuter high-level language. The latter
supports a floating-point format with a 32-bit mantissa and
a 16-bit exponent. A 32-bit mantissa is generally sufficient
considering the accuracy of the data obtained from the GPS
or GLONASS satellites. The corresponding file has an extension
.SRC and can be compiled into an .EXE file and executed on a
DSP computer equipped with the described dedicated DSP
hardware board, but with an unmodified CPU board!



l- 48 -
l
     In a portable GPS/GLONASS receiver all of the software
is stored in a 27C256 EPROM. The latter includes a starting
program, the high-level language compiler and a version of
the .SRC file with all of the comments and other unnecessary
symbols removed. When the portable receiver is turned on,
the program will be compiled in the RAM. This operation
takes around 10 seconds and is necessary to save EPROM space,
since the compiled program in the RAM takes around 100kbytes.
     The present discussion applies to the current software
versions V122 (GPS) or V39 (GLONASS). When running the
software on a DSP computer, the type of display may be
selected by the TOTAL/PARTIAL RESET switch while starting
the program: switch open (TOTAL RESET) selects the LCD
while switch closed (PARTIAL RESET) selects the CRT display.
Of course the LCD can only be selected in a stand-alone,
portable receiver and the corresponding input on the CPU
board MUST BE LEFT OPEN!

5.2. Real-time tasks: signal acquisition & processing
-----------------------------------------------------
     The signal acquisition and processing tasks run under the
1kHz interrupts requested by the dedicated DSP hardware
module. The tasks include the multiplexing of the
single-channel hardware among four different satellites,
the C/A-code synchronization acquisition and tracking,
the carrier lock acquisition and tracking, the 50bps
navigation-data demodulation, bit synchronization and frame
synchronization with parity check and finally the averaging
of the measured code phase, code rate and carrier frequency.
     After an interrupt request is received from the dedicated
DSP hardware, the interrupt-servicing routine will first latch
the content of all of the counters in the dedicated hardware.
It will then read the latched content and reset and arm the
interupt request flip-flop. The hardware counters are never
reset. The actually integrated value is computed from the
difference between the actual counter content and the previous
sample content. The four differences are further normalized
using the result from the reference 1ms divider. Finally,
the interrupt-servicing routine also increments a 32-bit
millisecond counter, which is later used to relate the
measurements to the 50bps navigation data.
     The single-channel hardware is multiplexed among all of
the satellites received. However, due to the limitations of
the hardware, switching to another satellite will corrupt
one millisecond of data. Therefore, the basic multiplexing
period includes one millisecond to switch the hardware
followed by 8 milliseconds to collect the data from a given
satellite. After this 9-millisecond period the hardware is
switched to another satellite. The multiplexing rate is
therefore 111 hops per second.
     The multiplexing rate and especially the multiplexing
sequence have to be chosen carefully. The navigation data
is transmitted at a speed of 50bps, so one bit is 20ms long
and lasts exactly 20 interrupt periods. If the navigation data
is to be collected from a given satellite, then this satellite
should get at least a few 1ms samples of data from each 20ms
bit period. Further, the multiplexing period should not be an
integer submultiple of the bit period, so that the bit
transitions can be detected.



l- 49 -
l
     Considering the limitations of the single-channel
hardware, the multiplexing sequence can not allow collecting
the navigation data from more than two satellites at a time.
In practice, since four satellites need to be received for a
navigation solution, the navigation data can only be collected
from a single satellite at a time using half of the
single-channel hardware time. The remaining hardware time
is split among the remaining three satellites. The priviliged
satellite that gets more hardware time of course needs to be
periodically exchanged to allow collecting the navigation data
from all four satellites.
     There is yet another constraint on the multiplexing
sequence. If a certain satellite only gets a few sampling
periods, then false locks of the carrier recovery loop
become very likely. In order to avoid this, the following
multiplexing sequence is used in the described GPS/GLONASS
receivers (1 = priviliged satellite, 2, 3 & 4 = others):

121213141412131314
121213141412131314
...

The complete multiplexing sequence therefore repeats after
18 multiplexing periods or 162 milliseconds.
     The C/A-code synchronization is always obtained from the
signal magnitude obtained from the dedicated hardware. The
signal phase information is intentionally not used for this
purpose since the carrier phase lock is a much more critical
operation. Therefore, for the C/A-code synchronization, the
early and late magnitudes are computed from the related I and
Q sums for every 1ms accumulation period. These sums are then
averaged over the 8 milliseconds containing valid data in a
9-millisecond multiplexing period.
     The initial state of the receiver is unlocked and the
C/A-code synchronization acquisition has to be obtained first.
The hardware variable delay will therefore be scanned through
all possible C/A-code phases (1023 for GPS and 511 for
GLONASS) by incrementing the variable-delay counter in suitable
steps (6 for GPS or 9 for GLONASS). When a signal magnitude
above treshold is detected, the software switches to the
synchronization maintaining routine. A suitable time constant
is built-in to prevent the loss of lock on short signal
interruptions. In the synchronization-tracking mode, the
software performs as a second-order phase-locked loop,
computing the C/A-code phase and rate from the measured
early-minus-late difference.
     The signal carrier still includes the 50bps 0/180 BPSK
navigation data, so a Costas-loop demodulator is required
to obtain both the regenerated carrier for doppler
measurements and the 50bps navigation data. The Costas-loop
demodulator operates on every 1ms signal sample I & Q
components computed as an average of the early/late data.
The loop feedback is a second-order network computing the
carrier phase and frequency.
     The carrier-lock operation is not simple. Initially,
the whole frequency range from -500Hz to +500Hz is
scanned. To prevent false locks, the scanning is stopped
only when the residual loop error becomes small enough.
Finally, the locking point needs to be checked for the



l- 50 -
l
+/-500Hz ambiguity caused by the 1kHz sampling rate. The
latter ambiguity is resolved by counting the number of
transitions in the demodulated data stream in every
8 milliseconds of valid data in a multiplexing period. Since
valid GPS data only has transitions every 20ms (GLONASS
every 10ms), there can be at most one transition in 8ms
of data. If the frequency is wrong, there are at least 6
transitions and this can be detected easily.
     Of course, the phases of both code and carrier PLLs
need to be adjusted for the following multiplexing period,
accounting for all of the time spent by the hardware
processing the signals from other satellites.
     In a navigation receiver the code phase and the carrier
frequency are the main parameters to be measured and these are
supplied by the corresponding phase-locked loops. In addition
to this, the code rate is also used by the software to
compute a rough approximation for the carrier frequency and
eliminate the ambiguity caused by the 1kHz signal sampling
rate. Before further processing, the code phase, code rate and
carrier frequency are averaged over 16 multiplexing periods
corresponding to a time span of 288ms (priviliged satellite)
or 864ms (other satellites). The averaged measurements are
placed in a FIFO memory together with 1ms time tags, to be
read by the main program.
     The last task performed by the interrupt routine is
navigation data processing. The latter includes yet another
PLL for bit synchronization. This PLL locks on the transitions
in the data stream. The demodulated 1ms samples containing
the transitions are rejected while all of the other available
samples for a given satellite are accumulated into bits (GPS)
or half-bits (the GLONASS manchester phase is not known yet).
     The following navigation data processing depends on the
data format and this is slightly different between GPS and
GLONASS. The GPS data is formatted into 30-bit words
containing 24 true data bits and 6 parity-check bits. The word
synchronization is obtained by checking the parity bits,
including the last two bits of the previous word, for any
possible word phase. The BPSK polarity ambiguity is also
resolved by the parity bits. The synhronized and checked
GPS data words are placed in another FIFO memory together with
1ms time tags, to be read by the main program.
     The GLONASS data is formatted into lines with 85 data
bits in manchester format and a non-manchester sync pattern,
for a total duration corresponding to 100 bits. The sync
pattern is not used in the described GLONASS receiver. The
synchronization is obtained by checking the 8 parity bits for
any possible half-bit phase (200 possible phases), to resolve
the manchester phase ambiguity as well. Since the data bits
are differentially encoded, there is no polarity ambiguity to
be resolved. Like in the GPS receiver, the correctly received
data lines are placed in another FIFO memory together with 1ms
time tags, to be read by the main program.

5.3. Main program loop tasks
----------------------------
     Since most of the functions performed by the main program
loop require high-accuracy floating-point arithmetics, the main
program is mainly written in the DSP computer high-level
language. Of course all of the interfaces to the interrupt



l- 51 -
l
routine and to the various peripherals (initialization of the
dedicated DSP hardware, LCD drive, real-time clock chip) are
at least partially written directly in the MC68010 machine
code and are inserted in hexadecimal format in the program
source code.
     The main program loop executes once for every new set
of averaged measured data. The latter is available every
864 milliseconds for the three satellites that get less
hardware time. The priviliged channel supplies three
separate sets of averaged data in the same time period, but
the excess data is not used by the main program loop.
     The main program loop also updates the LCD or writes a
new line on a CRT display. The internal operation of the
program is however independent of the selected menu on the
display. The menu only affects the keyboard functions and
some computations closely related to the format of the
displayed data, like coordinate conversions.
     The first task of the main program loop is to write the
look-up tables in the dedicated DSP hardware memory. This
operation is done at receiver power-up, when changing
satellites, when adjusting the carrier frequency (in 1kHz
steps) or when switching the priviliged satellite. The
satellites can be selected manually, but usually the software
is set to automatically select visible satellites.
     When a given satellite is selected, the receiver
requires some time to lock on its signal. The software will
first look for all possible C/A-code phases. If the lock is
not acheived, the main program loop will change the hardware
look-up table frequency in 1kHz steps in a given frequency
range (20kHz in the GPS receiver or 25kHz in the GLONASS
receiver). Of course the look-up table frequencies for all
four satellites can also be preset manually.
     The look-up tables are rewritten when switching the
priviliged satellite for several reasons. When all four
satellites have been acquired, this happens every minute,
synchronized to the major data frames transmitted every 30
seconds from both GPS and GLONASS satellites. Since switching
the priviliged satellite includes some loss of data, other
operations that corrupt the data, like rewriting the look-up
tables, may be performed at the same time without any
additional losses. The look-up tables are rewritten to correct
for large variations of the doppler shift or local reference
oscillator drift. Further, the new look-up tables are
rewritten with a randomly chosen phase relationship between
the carrier phase and code phase, to avoid any possible
interferences between the carrier and the code when averaging
the measured data over a longer period of time.
     The main loop will then process all of the navigation
data accumulated in the corresponding FIFO memory. The
software looks for the frame sync and formats the data into
frames. Additional checks are made before the formatted
data is used. Correctly received frames are used to collect
the precision ephemeris orbital data for the given satellite,
to update the almanac containing less accurate data about the
whole satellite navigation system and to set the GPS/GLONASS
receiver real-time clock chip.
     The next task is to collect the code phase and carrier
frequency measurement results from the corresponding FIFO
memory. The most recent data is always used together with the



l- 52 -
l
previous sample to relate all of the data to a single time
point using linear interpolation. This simplifies the
following computations, since the positions and velocities
of all four satellites need to be calculated for a single
point in time.
     The measured data and the satellite positions and
velocities (computed from the precision ephemeris data) are
then assembled into the navigation equations. A set of
three time-difference navigation equations is obtained from
code-phase differences and another set of three
doppler-difference navigation equations is obtained from
carrier-frequency differences.
     The time-difference navigation equations are solved
first, using the Newton's method. The starting point is taken
in the Earth's center (x=y=z=0). From this starting point
the Newton's method requires between three and four iterations
to converge to the final result for a user located on the
Earth's surface. The result in cartesian coordinates x,y,z
is then converted to longitude, latitude and height.
     The position obtained may now be corrected for the
propagation anomalies in the ionosphere and troposphere.
The present software does not apply any correction for the
ionosphere. The navigation equations are only corrected for
the troposphere at the caluculated height and the Newton's
method is iterated once again to obtain the final result.
     Since the position is already available from the
time-difference navigation equations, the doppler-difference
navigation equations are solved to obtain the velocity of
the user. Solving the doppler-difference equations for the
velocity does not require a numerical iterative method, since
the equations result linear for this unknown. The computed
velocity vector is converted into magnitude, azimuth and
elevation on the display.
     The accuracy of the navigation solution depends on the
geometry of the satellites. In place of the GDOP the software
only computes the determinant of the linearized system of
equations at the caluculated position. This determinant is
a dimensionless quantity. The higher the determinant, the
more accurate the solution. If the determinant is too low,
an error condition is signalled. The doppler-difference
equations have the same determinant if solved for velocity.
     The main program loop also performs data averaging.
Both position and velocity are averaged. Only good data
with no error signalled is added to the average. The
determinant of the system of equations is used as a weight
for each new data set added to the average. Of course the
averaging buffer may be manually reset if desired.
     The display includes several different menus and two
of them are devoted to the immediate and averaged data. The
position may be displayed in different formats: degrees
only, degrees, minutes and seconds or Gauss-Krueger
rectangular grid. Other menus are used to show the receiver
status and the almanac data.
     Finally, the main program loop usually also performs an
automatic satellite selection. This function is triggered
if an error condition is signalled continuously for a certain
period of time (100 main loops). The software then uses the
almanac data and the real-time clock to find the visible
satellites at the averaged user location. The receiver is



l- 53 -
l
then programmed for the four visible satellites with the
highest elevations on the sky. Although this procedure does
not yield the best GDOP, its operation is foolproof.

5.4. Software menus and commands
--------------------------------
     Since a portable GPS/GLONASS receiver only has a small
keyboard with a few keys and a small alphanumeric display,
the various user commands need to be arranged into several
different menus. The organization of the commands in the
different menus is shown on Fig. 62.
     The keyboard has 8 different keys. Four of them
(corresponding to ASCII characters "4", "5", "6" and "7") are
used to select the four main menus. Depressing these keys
only changes the content of the display and the functions of
the other keys, but does not affect the internal operation
of the GPS/GLONASS receiver. Some of these keys have
additional functions if depressed more than once. Depressing
key "4" cyclically shows all four virtual receiver channels
(satellites) on the display. Depressing key "7" cyclically
shows the general receiver status and the almanac data for
all currently visible satellites.
     The remaining keys (ASCII "0", "1", "2" and "3") are
called parameter keys. Depressing these keys affects the
internal operation of the GPS/GLONASS receiver as a function
of the current menu. The mode of operation of these keys is
also dependent on the actual menu. Some functions allow a
repeated action of these keys during just one main progran
loop (864ms), like setting the channel IF. Other functions
are intentionally slowed down, like the total reset of the
receiver. The latter requires depressing the corresponding
key for at least 9 times and just one entry is allowed for
each main program loop, to avoid unintentional loss of data.
     In order to understand the commands of a GPS/GLONASS
receiver it is necessary to understand the internal operation
of the latter. A GPS/GLONASS receiver includes a nonvolatile
RAM to store the almanac data and a real-time clock that
are always powered by a small internal NiCd battery. The
nonvolatile RAM is used to store the almanac data and the
approximate user position as a result of previous receiver
operation. At power-up this data is used together with the
real-time clock data to find all visible satellites and
speed-up the acquisition of four usable satellite signals.
     When a GPS or GLONASS receiver is first powered up,
all of the nonvolatile RAM contains random data and a total
reset is required. The total reset erases all almanac data
and puts the receiver in the manual satellite select mode.
All receiver virtual channels are set to a central carrier
frequency and GPS PRN#16 or GLONASS CHN#13. The menu "4"
is selected to show the virtual channel #1 data.
     The initial satellite signal acquisition without any
almanac data may take a large amount of time, especially in a
single-channel receiver. The receiver does not know which
satellite to look for nor its frequency offset caused by the
doppler shift and by the unknown frequency drift of the
receiver itself. The current software for the described
GPS/GLONASS receiver is not able to select different
satellites automatically without any almanac data, so this
has to be done manually.



l- 54 -
l
     After manually selecting the satellite(s), the software
is going to try to acheive C/A-code lock. If the latter does
not occur on the given IF frequency, the receiver is going to
scan the expected IF frequency range in 1kHz steps by writing
the corresponding look-up table. Only the priviliged satellite
IF is scanned in the range from 2310kHz to 2330kHz (GPS) or
from 1675kHz to 1700kHz (GLONASS).
     While searching for the initial signal acquisition there
is a small difference between the GPS and GLONASS receivers.
The GPS constellation is now complete and more than four
visible satellites can be found at any time, so the GPS
receiver is only going to switch the priviliged channel after
a satellite signal is acquired. On the other hand, the GLONASS
constellation is not complete and sometimes there is just one
visible satellite, so the GLONASS receiver is going to try
a different virtual channel with a different satellite if the
current priviliged satellite was not acquired.
     After a satellite signal has been acquired, the key "4"
menu shows the most important receiver parameters:

RX:    virtual channel number
SV:    GPS satellite PRN code number
CH#    GLONASS satellite RF channel number
CF:    look-up table preset central IF frequency (kHz)
R:     measured IF frequency (kHz, from code rate)
S:     signal level (S-meter)
SVH:   satellite health flag (0=OK)
URA:   GPS user range accuracy (m)
ASF:   GPS anti-spoofing flag (0=OFF)
En:    GLONASS ephemeris upload age (days)
AOE:   GLONASS ephemeris age (s)

     If the receiver has been turned on for the first time or
has not been used for a considerable period of time (more than
one week), the best thing to do is to collect the complete
almanac data first. To speed-up the almanac data collection
it is recommended that the remaining three receiver virtual
channels are set to the same satellite and to the same IF
frequency as the channel that already acquired a satellite.
After all four virtual channels acheived signal lock, the
almanac data collection takes 12.5 minutes for GPS or
5 minutes for GLONASS, since the GLONASS receiver does not
make use of half of the almanac frames.
     The accumulated almanac data can be checked by repeatedly
pressing key "7". The almanac data includes the satellite
name/number plus the following information:

CH#    GLONASS RF channel number
EL:    elevation (degrees)
AZ:    azimuth (degrees)
DF:    doppler frequency shift (Hz, polarity as in the IF)
A/E    GPS almanac/precision ephemeris data
SVH:   satellite almanac health flag (GPS 0=OK, GLONASS 1=OK)
ASF:   GPS anti-spoofing & configuration flag
UTC:   UTC date and time

     The elevation, azimuth and doppler shift are computed for
the reference user position as obtained from the averaged data.
After a total reset this reference position is set in central



l- 55 -
l
Europe. Checking the almanac it is possible to find out when
the receiver can be switched to automatic satellite selection.
In the automatic satellite selection mode, the program selects
the four satellites with the highest elevations and sets the
corresponding central IF values in the hardware look-up tables.
This selection can be done immediately by pressing key "0" in
menu "7" or by switching the program to do this automatically
after a period of bad data (key "3" in menu "7").
     After four satellites have been acquired, the display may
be switched to menu "5" or "6", to show respectively the
immediate or averaged data. These menus show the following:

DET:    determinant of the system of equations (menu "5" only)
AVG:    averaging weight (menu "6" only)
V:      velocity vector magnitude (km/h), azimuth & elevation
LAT:    latitude (degrees or m, north)
LON:    longitude (degrees or m, east)
H:      height above ellipsoid (m)

     At the beginning of all menus (except the almanac) the
receiver status error codes appear, as shown on Fig. 63. These
codes show the general receiver status, the current priviliged
virtual channel and the status of the single virtual channels.
Most of the codes used are obvious, but three of them require
further explanation. In the general receiver status, code "P"
means that the computed position deviates too much from the
previous main program loop. On the other hand, code "E" is
only activated after the averaging weight gets larger than 5
and means that the equations themselves deviate too much from
the already computed average position. Finally, code "T" in
the virtual channel status appears quite frequently since the
current software does not handle the overflow of the C/A-code
variable-delay counter correctly.
     Finally, the general status menu (key "7") shows some
intertesting data about the receiver: the satellites currently
selected, AUTomatic or MANual satellite selection, the
measured nominal IF frequency of the receiver (without the
doppler shift), the measured receiver master oscillator
frequency and the UTC date and time.























l- 56 -
l
6. Conclusion
=============
     The GPS and GLONASS systems are mainly intended for
navigation, but there are many other less advertised but not
less important nor less interesting applications of these
systems. Since these systems are known and the technology to
use them is available to anyone, we radio-amateurs should
consider our own applications of these systems [13].
     Although the navigation itself is not of much interest to
radio-amateurs, it would probably make much more sense to
transmit GPS or GLONASS coordinates of a contest location
rather than the inaccurate EU or WW locator, which is
already not accurate enough for serious microwave or laser
communications. By the way, GPS and GLONASS use almost the
same coordinate system and a long time average shows
differences in the order of only 10m between the two
systems.
     A side product of both GPS and GLONASS is accurate
time and frequency broadcast. In order to acheive the
specified navigation accuracy, the timing measurements have
to be performed to an accuracy of about 10ns. The same
requirement applies to the onboard satellite atomic clocks.
The final user time transfer accuracy ranges between 30ns
and 100ns, depending also on the knowledge of the exact user
location. Thus the user should also compute his position
even if he only needs accurate time.
     Radio-amateurs could use this time transfer capability
of both GPS or GLONASS every time when accurate synchronization
is required. Coherent communications are just an example, the
accuracy of GPS or GLONASS offers more than this: for example,
the actual propagation path of the radio signal and the
propagation mechanism could be investigated in this way.
     The frequency broadcast accuracy of both GPS and GLONASS
is in the range of 10^-12, far better than can be acheived
with HF or LF standard frequency transmitters. The accuracy
of the latter is limited to around 10^-7 by the propagation
effects alone, and this is not enough for serious microwave
work. GPS and GLONASS are also available globally 24 hours
per day and are not limited by the transmitter range,
propagation effects or low-frequency electronic pollution.
     Finally, GPS and GLONASS represent a step away from
being just an operator of black-box amateur-radio equipment.
Although there are several ready-made GPS receivers on the
market, we will probably have to develop our own receivers
for our experiments, both the hardware and the software.
Building such a receiver may be an interesting challenge as
well. The receiver shown in this article is perhaps just
the first step, other related projects or better receivers
will hopefully follow soon.













l- 57 -
l
7. References
=============

  [1] Matjaz Vidmar: "Digitale Signalverarbeitungs-Techniken
      fuer Funkamateure, Teil 2: Ein DSP-Computer fuer
      Amateurfunk-Anwendungen",
      pages 2-25/1-89, UKW-Berichte/VHF-Communications.

  [2] Matjaz Vidmar: "Digitale Signalverarbeitungs-Techniken
      fuer Funkamateure, Teil 3: Bau und Inbetriebnahme des
      Computers",
      pages 66-88/2-89, UKW-Berichte/VHF-Communications.

  [3] Jonathan S. Abel, James W. Chaffee: "Exsistence and
      Uniquiness of GPS Solutions",
      pages 952-956/6-91, VOL.27, IEEE TRANS. ON AEROSPACE AND
      ELECTRONIC SYSTEMS.

  [4] "Interface Control Document MH08-00002-400, rev. E",
      (84 pages), August 7th, 1975,
      Rockwell International Corporation, Space Division,
      12214 Lakewood Boulevard, Downey, California 90241, USA.

  [5] "Interface Control Document GPS-200",
      (102 pages), November 20th, 1981,
      Rockwell International, Space Operations and Satellite
      Systems Division, 12214 Lakewood Boulevard, Downey,
      California 90241, USA.

  [6] "Global Satellite Navigation System GLONASS Interface
      Control Document",
      (46 pages), 1988,
      Research-and-Production Association of Applied Mechanics,
      Institute of Space Device Engneering, GLAVKOSMOS, USSR.

  [7] Robert C. Dixon: "Spread Spectrum Systems",
      (422 pages), 1984, Second Edition,
      John Wiley & Sons, New York, USA.

  [8] Matjaz Vidmar: "Digital Signal Processing Techniques for
      Radio Amateurs, Theoretical Part",
      pages 76-97/2-88, VHF-Communications/UKW-Berichte.

  [9] P. Mattos: "Global Positioning by Satellite",
      (16 pages), Inmos, Technical note 65, July 1989.

 [10] J. B. Thomas: "Functional Description of Signal
      Processing in the Rogue GPS Receiver",
      (49 pages), June 1, 1988, Jet Propulsion Laboratory,
      California Institute of Technology, Pasadena,
      California, USA.

 [11] Charles C. Kilgus: "Shaped-Conical Radiation Pattern of
      the Backfire Quadrifilar Helix",
      (pages 392-397), IEEE Transactions on Antennas and
      Propagation, May 1975.






l- 58 -
l
 [12] Matjaz Vidmar: "Ein sehr rauscharmer Antennenverstarker
      fuer das L-band",
      pages 163-169/3-91, UKW-Berichte/VHF-Communications.

 [13] Matjaz Vidmar: "Radio-amateur applications of GPS/GLONASS
      satellites: Using GPS/GLONASS satellites as an accurate
      frequency/time standard",
      pages 186-190/Scriptum der Vortraege, 37. Weinheimer UKW
      Tagung, 19.-20. September 1992.





















































l- 59 -
l
8. List of figures
==================

Fig.  1 - Principle of hyperbolic navigation
Fig.  2 - Time and Doppler navigation equation
Fig.  3 - Altitude and inclination of GPS and GLONASS satellite
          orbits.
Fig.  4 - Published GPS satellite operation.
Fig.  5 - Recently observed GLONASS satellite operation.
Fig.  6 - GPS/GLONASS satellite block diagram.
Fig.  7 - GPS & GLONASS RF channel carrier frequencies.
Fig.  8 - GPS C/A-code generator.
Fig.  9 - GPS C/A-code shift register G2 tap selection.
Fig. 10 - GLONASS C/A-code generator.
Fig. 11 - Principle block diagram of a GPS/GLONASS receiver.
Fig. 12 - Principle block diagram of an 1-bit DSP GPS/GLONASS
          receiver.
Fig. 13 - GPS receiver block diagram.
Fig. 14 - GLONASS receiver block diagram.
Fig. 15 - GPS/GLONASS dedicated DSP hardware block diagram.
Fig. 16 - Quadrifilar backfire helix (RHCP).
Fig. 17 - Two-stage L-band LNA schematic.
Fig. 18 - Two-stage L-band LNA layout.
Fig. 19 - GPS RF module.
Fig. 20 - GPS RF module, upper side (top view).
Fig. 21 - GPS RF module, component location.
Fig. 22 - GPS IF converter, multiplier and mixer.
Fig. 23 - GPS IF converter, local oscillator.
Fig. 24 - GPS IF converter, bottom view.
Fig. 25 - GPS IF converter, component location.
Fig. 26 - GLONASS RF module.
Fig. 27 - GLONASS RF module, upper side (top view).
Fig. 28 - GLONASS RF module, component location.
Fig. 29 - GLONASS IF converter.
Fig. 30 - GLONASS IF converter, bottom view.
Fig. 31 - GLONASS IF converter, component location.
Fig. 32 - GLONASS PLL synthesizer converter.
Fig. 33 - GLONASS PLL synthesizer converter, upper side (top
          view).
Fig. 34 - GLONASS PLL synthesizer converter, component 
          location.
Fig. 35 - GLONASS synthesizer logic.
Fig. 36 - GLONASS synthesizer logic, bottom view.
Fig. 37 - GLONASS synthesizer logic, component location.
Fig. 38 - GPS/GLONASS second IF amplifier.
Fig. 39 - GPS/GLONASS second IF amplifier, bottom view.
Fig. 40 - GPS/GLONASS second IF amplifier, component location.
Fig. 41 - GPS/GLONASS DSP hardware (part 1).
Fig. 42 - GPS/GLONASS DSP hardware (part 2).
Fig. 43 - GPS/GLONASS DSP hardware, upper side (top view).
Fig. 44 - GPS/GLONASS DSP hardware, lower side (bottom view).
Fig. 45 - GPS/GLONASS DSp hardware, component location.
Fig. 46 - CPU board circuit diagram (part 1).
Fig. 47 - CPU board circuit diagram (part 2).
Fig. 48 - GPS/GLONASS CPU, upper side (top view).
Fig. 49 - GPS/GLONASS CPU, lower side (bottom view).
Fig. 50 - GPS/GLONASS CPU, component location.
Fig. 51 - 8-key keyboard.
Fig. 52 - 8-key keyboard, bottom view.



l- 60 -
l
Fig. 53 - 8-key keyboard, component location.
Fig. 54 - LCD backlight supply.
Fig. 55 - LCD backlight supply, bottom view.
Fig. 56 - LCD backlight supply, component location.
Fig. 57 - Power supply and RESET circuit.
Fig. 58 - Power supply and RESET circuit, bottom view.
Fig. 59 - Power supply and RESET circuit, component location.
Fig. 60 - Portable GPS receiver, module location.
Fig. 61 - Portable GLONASS receiver, module location.
Fig. 62 - GPS/GLONASS receiver software commands.
Fig. 63 - GPS/GLONASS receiver status error codes.